Ann Arbor Energy Commission

Solar Access Rights Subcommittee - Charter

BACKGROUND / PURPOSE

On March 4, 2019, the Ann Arbor City Council unanimously approved an Energy Commission (AAEC) resolution (attached as Reference 1) concerning the formation of diverse group of City staff, various Commission members, and general public to explore solar access rights, and either (1) define ordinance language to formally protect solar access from adjacent new construction/rehabilitation or vegetation growth, or (2) report out on recommended next steps if any.  This solar access resolution stemmed from recent advent of new vertical construction downtown that prevents existing adjacent solar PV arrays owned by others from accessing the sun.

SUBCOMMITTEE RESOURCES (at Formation)

At an April, 2019 AAEC meeting, discussion on Subcommittee membership identified that Hookham, Appleyard, and Clevey from AAEC were interested in serving along with MacDonald from City’s Sustainability and Innovation staff.  Other planned stakeholders include representatives from City staff, City Attorney’s office, Planning Commission, and general public.  Since many of these resources are employed by the City, MacDonald took actions to: (1) identify remaining City staff that will participate; (2) start a new Google Docs or “share point” site to house relevant documentation; and (3) post future Subcommittee meeting notices on Legistar to facilitate general public’s access to future meetings and direct participation.  Hookham will gauge interest in participation from City residents and businesses.

The Subcommittee will not receive any additional resources from the City, beyond voluntary time contributed by members, space at City Hall for meeting, and use of website (Google Docs) for communications and documents produced.

SUBCOMMITTEE TIMELINE

Consistent with the attached resolution, there is interest in this Solar Access Subcommittee completing its initial work in 2019 with an end-of-year submittal of a report (recommendations, ordinance language, other) to City Council.  Other milestone targets identified to support these schedule dates are listed below (actions to be monitored).

May 28, 2019 – Subcommittee Meeting – City Hall – 2nd Floor Workroom

June 14, 2019 – Finalize Subcommittee Resources (roster of participants)

August 1, 2019 – Subcommittee issues white paper summarizing access rights, alternatives to preserve such (e.g., ordinance, building permit action, other), and relevant background data, with comments and feedback due back September 6, 2019

October 1, 2019 – Subcommittee issues plan for remaining 2019 activities, based on September feedback, such as draft ordinance language or alternate next steps

November 10, 2019 – Proposed solar access ordinance language due to City Council for 2019 Action (or sunsetting of Subcommittee

Compliance with this Subcommittee’s timeline and production of well-thought products are viewed to be primary “SMART” goals.

KEY DEFINITIONS

Solar Access

Direct access to the sun’s rays without shading by a property owner desiring to install equipment used for collecting, transferring, converting, storing, or using incident solar energy for water heating, space heating, cooling, generating electricity, or other applications (“solar energy system”, or SES) that would otherwise require the use of a conventional source of energy (e.g., petroleum products, natural gas, or electricity produced from a nonrenewable resource).

Solar Easement

An agreement written, recognized by, and recorded with the county clerk or similar authority as a means to be legally binding representation of solar access. A solar easement needs to include a description of the dominant property that will benefit from the easement (e.g., where solar energy equipment is installed) and adjacent subservient property that will be encumbered by the easement, describing with specificity the angles or areas that must remain open to sunlight. The easement must also describe the specific height restrictions on walls, buildings, and vegetation as unambiguously as possible, as well as any seasonal/timing related restrictions.  Provisions describing the circumstances under which the easement can be modified or terminated are typically provided.

Solar Access Ordinance

Requirements identified in a jurisdiction code of ordinances governing said jurisdiction that describe minimum access to sunlight on properties and actions to be taken in the event that said access is to be restricted.

NATIONAL SURVEY ON SOLAR ACCESS

Per Reference 2, the 1978 Solar Rights Act in California created a legal framework for “solar access.” It included limited protections to allow consumers access to sunlight and to limit the ability of homeowner associations (HOA) and local governments from preventing installation of solar energy systems as well as provisions for use of “solar easements” or “solar access ordinances”.

Solar easements and ordinances in theory can ensure access to unobstructed sunlight for a solar energy system (SES); however, obtaining and negotiating a solar easement can be difficult and related ordinances can also be viewed as obstructions to development.  In lieu of an ordinance, easements are typically granted through a bilateral negotiation between neighboring landowners which can be contentious if there is a flat refusal to negotiate or to grant a solar easement. Further, easements can be burdensome and costly for individual homeowners to negotiate and legal costs could exceed the cost savings of the system if neighbors are not willing to grant the easement for free or nominal cost.  Depending on density, a prospective SES owner might have to negotiate with several neighbors to have access to sunlight. This is often the case in downtown city spaces or where multiple houses on a slope block access to sunlight. A greater number of parties negotiating typically increases cost and reduces the chance an easement will be created and in certain cases a solar easement is just not possible. More established neighborhoods were built with no consideration for the need of solar access. Even if parties are willing to negotiate for a solar easement, because of the design of the neighborhood, it may be impossible to place SESs so that they can be used efficiently.  An ordinance that dictates minimum responsibilities of parties involved have been shown to be more successful in avoiding easement-related disputes.

Clearly, a more formal easement procurement process or community ordinance that balances landowner’s right to feasibly install an SES and balances adjacency rights and development needs can lead to a more harmonized approach:

- Rights for an existing SES should not prevent adjacent construction/vegetation but should enable the SES owner to receive “consideration” if solar access is blocked by such;

- Rights for a future SES can be identified in a formal instrument such as an easement filed with county clerk or similar regulatory body that ensures that adjacent development consider “future solar access” in planning;

- Zoning districts that allow and encourage taller structures (above 2-stories) must carefully consider current infrastructure in-place and future solar access in land use planning

Many other states and communities have adopted ordinances and easement terms that can be studied and, where successful and adaptable, used as a starting point for the City of Ann Arbor (e.g., see References 2 and 3).  Reviewing such will be one of the Subcommittee’s first activities upon formation in 2019.  According to a survey of the Reference 4 DSIRE database, more than 40 states currently have some form of solar access or solar rights laws, but most are voluntary and simply allow (but do not mandate) neighbors to directly negotiate solar easements with each other.  California, Iowa, Massachusetts, and New Mexico are among the states that have taken varied approaches to solar access laws.

REFERENCES

- City of Ann Arbor, File No. 19-0394, Resolution Requesting City of Ann Arbor to Develop and Adopt a Solar Access Ordinance, approved by City Council on March 4, 2019.

- Kettles, C.M, “A Comprehensive Review of Solar Access Law in the United States – Suggested Standards for a Model Statute and Ordinance”, Solar America Board for Codes and Standards Report, U.S. Department of Energy (DOE) Award Number DE-FC36-07GO17034, October, 2018.

- National Renewable Energy Laboratory (NREL; under the DOE), “Solar Access: Issues and Policy Statements”, Alison Holm, June 6, 2017.

- NC Clean Energy Technical Center, “Database of State Incentives for Renewables & Efficiency (DSIRE)”, http://www.dsireusa.org/system/program