CONTRACT DOCUMENTS

FOR

Superior Dam Painting and Handrail Replacement Project

March 2008

FILE NO.   08003

BID NO. ITB-3931

WATER UTILITIES DEPARTMENT

### CITY OF ANN ARBOR

100 North Fifth Avenue

Ann Arbor, Michigan  48104

TABLE OF CONTENTS

Section																					Pages

Table of Contents	TC-1

Advertisement	AD-1

Human Rights Division Contract Compliance Forms	AAF-1 to 2

Living Wage Public Notice, Poster and Compliance Forms	LW-1 to 2

Notice of Pre-Bid Conference	NP-1

Instructions to Bidders	IB-1 to 3

Proposal	P-1 to 3

Bid Forms	BF-1 to 6

Contract	C-1 to 4

Bond Forms	B-1 to 2

General Conditions	GC-1 to 21

Supplemental Insurance Requirements	SI-1

Standard Specifications	SS-1

Detailed Specifications	DS-1 to 23

Supplemental Specifications	SP-1 to 2

Appendix A:

Detail Drawing Sheets	1 of 9 to 9 of 9

Appendix B:

Product Data	PD-1 to 4

ADVERTISEMENT FOR

FOR THE Superior Dam Painting and Handrail Replacement Project

CITY OF ANN ARBOR, MICHIGAN

BID NO.  ITB-3931

Sealed Bids will be received by the, Purchasing Division, Fifth Floor, City Hall, on or before     2:00 PM March 31, 2008, for the project of Superior Dam Painting and Handrail Replacement at Superior Dam.    Bids will be publicly opened and read aloud at this time.  A pre-bid conference will be held on March 19, 2008 at 10:00 AM at Superior Dam, 6000 First Street, Ypsilanti, Michigan.  Attendance is highly recommended.

Work to be done includes: painting preparation work and painting of sluice gate components and dam walkway structural steel; gate seal replacement; gate hoist chain replacement; transporting, installing and removing stop logs; fall protection equipment installation; fabrication and placement of a replacement machinery base and cover; placement of approximately 40 LF of new handrail; replacement of approximately 650 LF of existing handrail; and all related work.  Bid documents may be obtained on or after noon on March 10, 2008 from the office of the Purchasing Division, Fifth Floor, City Hall, Ann Arbor, Michigan.  Bid documents may also be obtained from the City of Ann Arbor’s website: http://www.a2gov.org/government/financeadminservices/procurement/Pages/OpenBidsandProposals.aspx

A fee of $25.00 per set of printed documents will be charged.  No refunds will be given for returned documents.

Each proposal shall be accompanied by a certified check, or Bid Bond by a recognized surety, in the amount of 5% of the total of the bid price. A proposal, once submitted, becomes the property of the City. In the sole discretion of the City, the City reserves the right to allow a bidder to reclaim submitted documents provided the documents are requested and retrieved no later than 48 hours prior to the scheduled bid opening.

The successful Bidder will be required to furnish satisfactory performance and labor and material bonds in the amount of 100% of the bid price and satisfactory insurance coverage.

Precondition for entering into a contract with the City of Ann Arbor is compliance with Chapter 112 of Title IX of the Code of the City of Ann Arbor.   The successful Bidder may also be required to comply with Chapter 23 of Title I of the Code of the City of Ann Arbor. Further information is outlined in the contract documents.

After the time of opening, no Bid may be withdrawn for a period of 90 days. The City reserves the right to accept any Bid, to reject any or all Bids, to waive irregularities and/or informalities in any Bid, and to make the award in any manner the City believes to be in its best interest.

Any further information may be obtained from the Purchasing Division, (734) 994-2719.

CITY OF ANN ARBOR, MICHIGAN

NOTICE OF PRE-BID CONFERENCE

A pre-bid conference for this project will be held on Wednesday, March 19, 2008 at 10:00 a.m. at Superior Dam, 6000 First Street, Ypsilanti, MI 48198.  Directions may be obtained by calling (734) 994-2840.

Attendance at this conference is highly recommended.  Administrative and technical questions regarding this project will be answered at this time.  If any questions arise whose answers constitute modifications to the bid documents, an addendum will be issued.

INSTRUCTIONS TO BIDDERS

General

Work to be done under this Contract is generally described through the detailed specifications and must be completed fully in accordance with the contract documents. All work to be done under this Contract is located in the City of Ann Arbor and at Superior Dam, 6000 First Street, Ypsilanti, MI 48198.

The City shall make available to all prospective Bidders, prior to receipt of the Bids, access to the area in which the work is to be performed. Advance notice should be given to the Administering Department in cases where access to the site must be arranged by the City.

Any proposal which does not conform fully with these instructions may be rejected.

Proposals

Proposals must be submitted on the "Proposal Forms" and "Bid Forms" provided, without removal from the binder, with each blank properly filled in.  Sealed proposals will be received by the City of Ann Arbor Purchasing Division, Fifth Floor, City Hall, Ann Arbor, Michigan, at the time stipulated in the Advertisement, promptly after which proposals will be publicly opened and read aloud.  Each proposal must be enclosed in a sealed envelope, endorsed across one end:

BID # ITB-3931, Proposal for Superior Dam Painting and Handrail Replacement Project

As part of the proposal, Bidders shall submit the attached form, “Section 5 – References”, which identifies a minimum of three projects, including construction cost and contact information, completed within the last five years that demonstrate similar work experience to that included within these contract documents, specifically bridge and/or dam painting projects.

The City will evaluate Proposals based on cost as well as experience.  Contractors that have not included the required list of similar work experience and associated references in Section 5 of the Bid Form may have their bid rejected.

The City intends to award a Contract(s) to the lowest responsible Bidder(s).  On multi-divisional contracts, separate divisions may be awarded to separate Bidders.  The City may also utilize discounts offered in the Bid Forms, if any, to determine the lowest responsible Bidder on each division, and award multiple divisions to a single Bidder, so that the lowest total cost is achieved for the City. For unit price bids, the contract will be awarded based upon the lump sum and unit prices stated by the bidder for the work items specified in the bid documents, with consideration given to any alternates selected by the City. If the City determines that the unit price for any item is materially different for the work item bid than either other bidders or the general market, the City, in its sole discretion, in addition to any other right it may have, may reject the bid as not responsible or non-conforming.

The acceptability of major subcontractors will be considered in determining if a Bidder is responsible.  In comparing proposals, the City will give consideration to alternate proposals for items listed in the forms, or other alternates which the Bidder may wish to submit, but preference will be given to Base Bid Proposals.

The City reserves the right to accept any Bid, to reject any or all Bids, to waive irregularities and/or informalities in any Bid, and to make the award in any manner the City believes to be in its best interest.

Bid Security

Each proposal must be accompanied by a certified check, or Bid Bond by a surety licensed and authorized to do business within the State of Michigan, in the amount of 5% of the total of the bid price.

Withdrawal of Bids

After the time of opening, no Bid may be withdrawn for the period of days specified in the Advertisement.

Contract Time

Time is of the essence in the performance of the work under this Contract.  The available time for work under this Contract is indicated on page C-1, Article III of the Contract.  If these time requirements can not be met, the Bidder must stipulate on Bid Form Section 3 - Time Alternate its schedule for performance of the work.  Consideration will be given to time in evaluating bids.

Liquidated Damages

A liquidated damages clause, as given on page C-2, Article III of the Contract, provides that the Contractor shall pay the City as liquidated damages, and not as a penalty, a sum certain per day for each and every day that the Contractor may be in default of completion of the specified work, within the time(s) stated in the Contract, or written extensions.

Liquidated damages clauses, as given in the General Conditions, provide further that the City shall be entitled to impose and recover liquidated damages for breach of the obligations under Chapter 112 of the City Code.

The liquidated damages are for the non-quantifiable aspects of any of the previously identified events and do not cover actual damages that can be shown or quantified nor are they intended to preclude recovery of actual damages in addition to the recovery of liquidated damages.

Human Rights Information

Section 5, beginning at page GC-3, outlines the requirements for fair employment practices under City of Ann Arbor Contracts.  To establish compliance with this Ordinance, the Bidder must complete and return with its bid completed copies of the white and pink Human Rights Division Contract Compliance Forms (copy attached) or an acceptable equivalent.

Wage Requirements

Section 4, beginning at page GC-2, outlines the requirements for payment of prevailing wages or of a “living wage” to employees providing service to the City under this contract. The successful bidder must comply with all applicable requirements and may be required to provide documentary proof of compliance.

Major Subcontractors

The Bidder shall identify each major subcontractor it expects to engage for this Contract if the work to be subcontracted is 15% or more of the bid sum or over $50,000, whichever is less.  The Bidder also shall identify the work to be subcontracted to each major subcontractor.

PROPOSAL

City of Ann Arbor

Guy C. Larcom Municipal Building

Ann Arbor, Michigan  48104

Ladies and Gentlemen:

The undersigned, as Bidder, declares that this Bid is made in good faith, without fraud or collusion with any person or persons bidding on the same Contract; that this Bidder has carefully read and examined the bid documents, including Advertisement, Human Rights Division Contract Compliance Forms, Notice of Pre-Bid Conference, Instructions to Bidders, Proposal, Bid Forms, Contract, Bond Forms, General Conditions, Standard Specifications, Detailed Specifications, all Addenda, and the Plans and understands them.  The Bidder declares that it conducted a full investigation at the site and of the work  proposed and is fully informed as to the nature of the work and the conditions relating to the work's performance.  The Bidder also declares that it has extensive experience in successfully completing projects similar to this one.

The Bidder acknowledges that it has not received or relied upon any representations or warrants of any nature whatsoever from the City of Ann Arbor, its agents or employees, and that this Bid is based solely upon the Bidder's own independent business judgment.

The undersigned proposes to perform all work shown on the plans or described in the bid documents, including any addenda issued, and to furnish all necessary machinery, tools, apparatus, and other means of construction to do all the work, furnish all the materials, and complete the work in strict accordance with all terms of the Contract of which this proposal is one part.

In accordance with these bid documents, and Addenda numbered               , the undersigned, as Bidder, proposes to perform at the sites in and/or around Ann Arbor, Michigan, all the work included herein for the amounts set forth in the Bid Forms.

The Bidder declares that it has become fully familiar with the liquidated damage clauses for completion times and for compliance with City Code Chapter 112, understands and agrees that the liquidated damages are for the non-quantifiable aspects of non-compliance and do not cover actual damages that may be shown and agrees that if awarded the Contract, all liquidated damage clauses form part of the Contract.

The Bidder declares that it has become fully familiar with the provisions of Chapter 14, Section 1:319 (Prevailing wages) and Chapter 23 (Living Wage) of the Code of the City of Ann Arbor and that it understands and agrees to comply, to the extent applicable to employees providing services to the City under this Contract, with the wage and reporting requirements stated in the City Code provisions cited. Bidder further agrees that the cited provisions of Chapter 14 and Chapter 23 form a part of this Contract.

The Bidder encloses a certified check or Bid Bond in the amount of 5% of the total of the Bid Price.  The Bidder agrees both to contract for the work and to furnish the necessary Bonds and insurance documentation within 10 days after being notified of the acceptance of the Bid.

If this Bid is accepted by the City and the Bidder fails to contract and furnish the required Bonds and insurance documentation within 10 days after being notified of the acceptance of this Bid, then the Bidder shall be considered to have abandoned the Contract and the certified check or Bid Bond accompanying this Proposal shall become due and payable to the City.

If the Bidder enters into the Contract in accordance with this Proposal, or if this Proposal is rejected, then the accompanying check or Bid Bond shall be returned to the Bidder.

In submitting this Bid, it is understood that the right is reserved by the City to accept any Bid, to reject any or all Bids, to waive irregularities and/or informalities in any Bid, and to make the award in any manner the City believes to be in its best interest.

SIGNED THIS                 DAY OF                          , 200   .

| _____________________________________ Bidder’s Name |  |
| --- | --- |
| _____________________________________ Official Address |

_____________________________________

| Authorized Signature of Bidder |
| --- |
| _____________________________________ Telephone Number | _____________________________________ (Print Name of Signer Above) |

LEGAL STATUS OF BIDDER

(The Bidder shall fill out the appropriate form and strike out the other two.)

Bidder declares that it is:

*  A corporation organized and doing business under the laws of the state of

, for whom                                                                      , bearing the office title of                                  , whose signature is affixed to this proposal,

is authorized to execute contracts.

*  A partnership, list all members and the street and mailing address of each:

Also identify the County and State where partnership papers are filed:

County of ___________________________ , State of ________________________________

*  An individual, whose signature with address, is affixed to this proposal:   ________

(initial here)

BID FORM

Section 1 - Schedule of Prices

Base Bid

While it is the City’s intent to complete the project substantially as specified, the City reserves the right to delete any of the items numbered 2 through 5 of the base bid identified below.

Item No. 1

For the complete work of:  building and maintaining a fully enclosed work area; preparing and painting all sluice gate components; moving, placing and removing stop logs; replacement of gate seals; and replacement of hoist chains as outlined within these documents, using materials only of the type and manufacturers where specifically named, and all associated work identified in the Contract Documents.

Dollars ($                             )

Item No. 2

The Contractor shall remove and dispose of existing handrail, prepare shop drawings for submittal to Owner for approval, furnish and place new handrail and guard chain as identified and specified within the Contract Documents.

______________________________________________________ Dollars ($_______________)

Item No. 3

The Contractor shall remove existing machinery cover and base, fabricate new galvanized steel cover and base, and place new machinery cover and base as specified within the Contract Documents.

_______________________________________________________ Dollars ($_______________)

Item No. 4

The Contractor shall install fall protection equipment furnished by the Owner in accordance with manufacturer’s recommendations and as specified within the Contract Documents.

_______________________________________________________ Dollars ($________________)

Item No. 5

For the complete work of:  removing and storing the dam walkway; building and maintaining a fully enclosed work area; preparing and painting all dam walkway structural steel members; replacing the dam walkway as outlined within these documents, using materials only of the type and manufacturers where specifically named, and all associated work identified in the Contract Documents.

_______________________________________________________ Dollars ($______________)

TOTAL BASE BID (Includes Items No.1-5)

_______________________________________________________ Dollars ($_______________)

Alternates

The following items are alternates for the material to be used to replace the machinery cover.  The Owner may elect to substitute one of the alternates below for Item No. 3 in the base bid.

Alternate 1 to Item No. 3

The Contractor shall remove existing machinery cover and base, fabricate new grade 304 stainless steel cover and base, and place new machinery cover and base as specified within the Contract Documents.

_______________________________________________________ Dollars ($______________)

Alternate 2 to Item No. 3

The Contractor shall remove existing machinery cover and base, fabricate new carbon steel cover and base, prepare and paint new machinery cover and base using materials only of the type and manufacturers where specifically named, and place new machinery cover and base as specified within the Contract Documents.

_______________________________________________________ Dollars ($_____________)

BID FORM

Section 2 - Material and Equipment Alternates

The Base Bid proposal price shall include materials and equipment selected from the designated items and manufacturers listed in the bidding documents. This is done to establish uniformity in bidding and to establish standards of quality for the items named.

If the Contractor wishes to quote alternate items for consideration by the City, it may do so under this Section.  A complete description of the item and the proposed price differential must be provided.  Unless approved at the time of award, substitutions where items are specifically named will be considered only as a negotiated change in Contract Sum.

Item Number                          Description                                             Add/Deduct Amount

If the Bidder does not suggest any material or equipment alternate, the Bidder MUST complete the following statement:

For the work outlined in this request for bid, the bidder does NOT propose any material or equipment alternate under the contract.

Signature of Authorized Representative of Bidder  ____________________________

BID FORM

Section 3 - Time Alternate

If the Bidder takes exception to the time stipulated in Article III of the Contract, Time of Completion, page C-1, it is requested to stipulate below its proposed time for performance of the work.  Consideration will be given to time in evaluating bids.

If the Bidder does not suggest any time alternate, the Bidder MUST complete the following statement:

For the work outlined in this request for bid, the bidder does NOT propose any time alternate under the contract.

Signature of Authorized Representative of Bidder  ____________________________

BID FORM

Section 4 - Major Subcontractors

For purposes of this contract, a Subcontractor is anyone (other than the Contractor) who performs work (other than or in addition to the furnishing of materials, plans or equipment) at or about the construction site, directly or indirectly for or on behalf of the Contractor (and whether or not in privity of contract with the Contractor), but shall not include any individual who furnishes merely the individual’s own personal labor or services.

For the work outlined in these documents the Bidder expects to engage the following major subcontractors to perform the work identified:

Subcontractor (Name and Address)                Work                                      Amount

If the Bidder does not expect to engage any major subcontractor, the Bidder MUST complete the following statement:

For the work outlined in this request for bid, the bidder does NOT expect to engage any major subcontractor to perform work under the contract.

Signature of Authorized Representative of Bidder  ___________________________

BID FORM

Section 5 – References

Include a minimum of three references from previously completed, similar work, within the past five years.

1)  _______________________________________________________            ________________

Project Name/Cost		Date Constructed

_______________________________________________________         ________________

Owner Contact Name		Phone Number

2)  _______________________________________________________            ________________

Project Name/Cost		Date Constructed

_______________________________________________________         ________________

Owner Contact Name		Phone Number

3)  _______________________________________________________            ________________

Project Name/Cost		Date Constructed

_______________________________________________________         ________________

Owner Contact Name		Phone Number

CONTRACT

THIS AGREEMENT is made on the _15th__ day of ___May___________, 2008_, between the CITY OF ANN ARBOR, a Michigan Municipal Corporation, 100 N. Fifth Avenue, Ann Arbor, Michigan 48104 (“City”) and __Atsalis Brothers Painting_____________________(“Contractor”)  A Michigan Corporation,       22189 East 14 Mile Road, Clinton Township, Michigan 48035

(An individual/partnership/corporation, include state of incorporation)                                  (Address)

Based upon the mutual promises below, the Contractor and the City agree as follows:

ARTICLE I - Scope of Work

The Contractor agrees to furnish all of the materials, equipment and labor necessary; and to abide by all the duties and responsibilities applicable to it for the project titled “Superior Dam Painting and Handrail Replacement Project” in accordance with the requirements and provisions of the following documents, including all written modifications incorporated into any of the documents, which are incorporated as part of this Contract:

| Human Rights Division Contract Compliance Forms Living Wage Declaration of Compliance Forms (if applicable) Bid Forms Proposal Contract and Exhibits Bonds | General Conditions Standard Specifications Detailed Specifications Plans Addenda |
| --- | --- |

ARTICLE II - Definitions

Administering Service Unit means Water Treatment Services/Public Services Area

Supervising Professional means Water Utility Engineer or other persons acting under the authorization of the Administrator of the Administering Service Unit.

Project means “Superior Dam Painting and Handrail Replacement Project, Bid No. ITB-3931”.

ARTICLE III - Time of Completion

(A)	       The work to be completed under this Contract shall begin immediately after the Contractor’s receipt of a fully executed Contract.

(B)	        The entire work for this Contract shall be completed within 120 consecutive calendar days.

(C)	        Failure to complete all the work within the time specified above, including any extension granted in writing by the Supervising Professional, shall obligate the Contractor to pay the City, as liquidated damages and not as a penalty, an amount equal to $500 for each calendar day of delay in the completion of all the work.  If any liquidated damages are unpaid by the Contractor, the City shall be entitled to deduct these unpaid liquidated damages from the monies due the Contractor.

As an independent requirement, where the Detailed Specification Section 01000, “GENERAL REQUIREMENTS”, identifies certain portions of the work to be completed within a shorter period of time and the Contractor fails to complete each portion within the shorter period specified for each portion, including any extension granted in writing by the Supervising Professional, the City is entitled to deduct from the monies due the Contractor, as liquidated damages and not as a penalty, the amount identified in the Detailed Specifications for each portion of the work not timely completed for each calendar day of delay in completion of each portion of the work.

The liquidated damages are for the non-quantifiable aspects of any of the previously identified events and do not cover actual damages that can be shown or quantified nor are they intended to preclude recovery of actual damages in addition to the recovery of liquidated damages.

Liquidated damages under this section are in addition to any liquidated damages due under Section 5 of the General Conditions.

ARTICLE IV - The Contract Sum

The City shall pay to the Contractor for the performance of the Contract, the lump sum price as given in the Bid Forms for the estimated total of:

Two Hundred Three Thousand Fourty and no/100__ Dollars ($_203,040.00_____)

The amount paid shall be equitably adjusted to cover changes in the work ordered by the Supervising Professional but not required by the contract documents.  Increases or decreases shall be determined only by written agreement between the City and Contractor.

ARTICLE V - Assignment

This Contract may not be assigned or subcontracted without the written consent of the City.

ARTICLE VI - Choice of Law

This Contract shall be construed, governed, and enforced in accordance with the laws of the State of Michigan.  By executing this agreement, the Contractor and the City agree to venue in a court of appropriate jurisdiction sitting within Washtenaw County for purposes of any action arising under this Contract.

Whenever possible, each provision of the contract will be interpreted in a manner as to be effective and valid under applicable law.  The prohibition or invalidity, under applicable law, of any provision will not invalidate the remainder of the contract.

ARTICLE VII - Relationship of the Parties

The parties of the Contract agree that it is not a contract of employment but is a contract to accomplish a specific result.  Contractor is an independent contractor performing services for the City.  Nothing contained in this Contract shall be deemed to constitute any other relationship between the City and the Contractor.

Contractor certifies that it has no personal or financial interest in the project other than the compensation it is to receive under the Contract.  Contractor certifies that it is not, and shall not become, overdue or in default to the City for any contract, debt, or any other obligation to the City  including real or personal property taxes. City shall have the right to set off any such debt against compensation awarded for services under this agreement.

ARTICLE VIII - Notice

All notices given under this contract shall be in writing, and shall be by personal delivery or by certified mail with return receipt requested  to the parties at their respective addresses as specified in the contract documents or other address the Contractor may specify in writing.

ARTICLE IX - Indemnification

To the fullest extent permitted by law, for any loss not covered by insurance under this contract, Contractor shall indemnify, defend and hold harmless the City, its officers, employees and agents harmless from all suits, claims, judgments and expenses including attorney’s fees resulting or alleged to result, in whole or in part, from any act or omission, which is in any way connected or associated with this contract, by the Contractor or anyone acting on the Contractor’s behalf under this contract. Contractor shall not be responsible to indemnify the City for losses or damages caused by or resulting from the City’s sole negligence.

ARTICLE X - Entire Agreement

This Contract represents the entire understanding between the City and the Contractor and it supersedes all prior representations or agreements whether written or oral. Neither party has relied on any prior representations in entering into this Contract. This Contract may be altered, amended or modified only by written amendment signed by the City and the Contractor.

| FOR CONTRACTOR | FOR THE CITY OF ANN ARBOR |
| --- | --- |
| By Its: _________________________ | By________________________ John Hieftje, Mayor |
|  | By________________________ Jacqueline Beaudry, City Clerk |
|  | Approved as to substance By __________________________ Roger W. Fraser, City Administrator |
|  | By___________________________ Sue F. McCormick, Public Services Area Administrator |
|  | Approved as to form and content ______________________________ Stephen K. Postema, City Attorney |

PERFORMANCE BOND

(1)	                                                                                                                                             of                                                                                                                                           (referred to as "Principal"), and                                                                                                   , a corporation duly authorized to do business in the State of Michigan (referred to as "Surety"), are bound to the City of Ann Arbor, Michigan (referred to as "City"), for 	$                                                                 ,  the payment of which Principal and Surety bind themselves, their heirs, executors, administrators, successors and assigns, jointly and severally, by this bond.

(2)	The Principal has entered a written contract with the City dated                                            , 200   , for:                                                                                                                                                                                            Superior Dam Painting and Handrail Replacement Project    and this bond is given for that contract in compliance with Act No. 213 of the Michigan Public Acts of 1963, as amended, being MCL 129.201 et seq.

(3)	Whenever the Principal is declared by the City to be in default under the contract, the Surety may promptly remedy the default or shall promptly:

(a)  complete the contract in accordance with its terms and conditions; or

(b)  obtain a bid or bids for submission to the City for completing the contract in accordance with its terms and conditions, and upon determination by Surety of the lowest responsible bidder, arrange for a contract between such bidder and the City, and make available, as work progresses, sufficient funds to pay the cost of completion less the balance of the contract price; but not exceeding, including other costs and damages for which Surety may be liable hereunder, the amount set forth in paragraph 1.

(4)	Surety shall have no obligation to the City if the Principal fully and promptly performs under the contract.

(5)	Surety agrees that no change, extension of time, alteration or addition to the terms of the contract or to the work to be performed thereunder, or the specifications accompanying it shall in any way affect its obligations on this bond, and waives notice of any such change, extension of time, alteration or addition to the terms of the contract or to the work, or to the specifications.

SIGNED AND SEALED this               day of                                , 200    .

| _______________________________________ (Name of Surety Company) | ___________________________________________ (Name of Principal) |
| --- | --- |
| By ____________________________________ (Signature) | By ________________________________________ (Signature) |
| Its _____________________________________ (Title of Office) | Its ________________________________________ (Title of Office) |
| Approved as to form: _______________________________________ Stephen K. Postema, City Attorney | Name and address of agent: __________________________________________ __________________________________________ |

LABOR AND MATERIAL BOND

(1)	                                                                                                                                  of                                                                                                                              , (referred to as "Principal"), and                                                                                         , a corporation duly authorized to do business in the State of Michigan, (referred to as "Surety"), are bound to the City of Ann Arbor, Michigan (referred to as "City"), for the use and benefit of claimants as defined in Act 213 of Michigan Public Acts of 1963, as amended, being MCL 129.201 et seq., in the amount of $                                    , for the payment of which Principal and Surety bind themselves, their heirs, executors, administrators, successors and assigns, jointly and severally, by this bond.

(2)	The Principal has entered a written contract with the City, dated                                 , 200    , for                Superior Dam Painting and Handrail Replacement Project ;  and this bond is given for that contract in compliance with Act No. 213 of the Michigan Public Acts of 1963 as amended;

(3)	If the Principal fails to promptly and fully repay claimants for labor and material reasonably required under the contract, the Surety shall pay those claimants.

(4)	Surety's obligations shall not exceed the amount stated in paragraph 1, and Surety shall have no obligation if the Principal promptly and fully pays the claimants.

SIGNED AND SEALED this               day of                            , 200     .

| ______________________________________ (Name of Surety Company) | _______________________________________ (Name of Principal) |
| --- | --- |
| By ___________________________________ (Signature) | By _____________________________________ (Signature) |
| Its ____________________________________ (Title of Office) | Its _____________________________________ (Title of Office) |
| Approved as to form: ______________________________________ Stephen K. Postema, City Attorney | Name and address of agent: _______________________________________ ________________________________________ |

GENERAL CONDITIONS

Section 1 - Execution, Correlation and Intent of Documents

The contract documents shall be signed in 2 copies by the City and the Contractor.

The contract documents are complementary and what is called for by any one shall be binding.  The intention of the documents is to include all labor and materials, equipment and transportation necessary for the proper execution of the work. Materials or work described in words which so applied have a well-known technical or trade meaning have the meaning of those recognized standards.

In case of a conflict among the contract documents listed below in any requirement(s), the requirement(s) of the document listed first shall prevail over any conflicting requirement(s) of a document listed later.

(1) Addenda in reverse chronological order; (2) Detailed Specifications; (3) Standard Specifications;  (4) Plans; (5) General Conditions; (6) Contract; (7) Bid Forms; (8) Bond Forms; (9) Proposal.

Section 2 - Order of Completion

The Contractor shall submit with each invoice, and at other times reasonably requested by the Supervising Professional, schedules showing the order in which the Contractor proposes to carry on the work.  They shall include the dates at which the Contractor will start the several parts of the work, the estimated dates of completion of the several parts, and important milestones within the several parts.

Section 3 - Familiarity with Work

The Bidder or its representative shall make personal investigations of the site of the work and of existing structures and shall determine to its own satisfaction the conditions to be encountered, the nature of the ground, the difficulties involved, and all other factors affecting the work proposed under this Contract. The Bidder to whom this Contract is awarded will not be entitled to any additional compensation unless conditions are clearly different from those which could reasonably have been  anticipated by a person making diligent and thorough investigation of the site.

The Bidder shall immediately notify the City upon discovery, and in every case prior to submitting its Bid, of every error or omission in the bidding documents that would be identified by a reasonably competent, diligent Bidder. In no case will a Bidder be allowed the benefit of extra compensation or time to complete the work under this Contract for extra expenses or time spent as a result of the error or omission.

Section 4 - Wage Requirements

Under this Contract, the Contractor shall conform to Chapter 14 of Title I of the Code of the City of Ann Arbor as amended; which in part states "...that all craftsmen, mechanics and laborers employed directly on the site in connection with said improvements, including said employees of subcontractors, shall receive the prevailing wage for the corresponding classes of craftsmen, mechanics and laborers, as determined by statistics for the Ann Arbor area compiled by the United States Department of Labor.  At the request of the City, any contractor or subcontractor shall provide satisfactory proof of compliance with the contract provisions required by the Section."

Where the Contract and the Ann Arbor City Ordinance are silent as to definitions of terms required in determining contract compliance with regard to prevailing wages, the definitions provided in the Davis-Bacon Act as amended  (40 U.S.C. 278-a to 276-a-7) for the terms shall be used.

Further, to the extent that any employees of the Contractor providing services under this contract are not part of the class of craftsmen, mechanics and laborers who receive a prevailing wage in conformance with Section 1:319 of Chapter 14 of Title I of the Code of the City of Ann Arbor, the Contractor agrees to conform to Chapter 23 of Title I of the Code of the City of Ann Arbor, as amended, which in part states:

1:814.  Applicability.

(1)	This Chapter shall apply to any person that is a contractor/vendor or grantee as defined in Section 1:813 that employs or contracts with five (5) or more individuals; provided, however, that this Chapter shall not apply to a non-profit contractor/vendor or non-profit grantee unless it employs or contracts with ten (10) or more individuals.

(2)	This Chapter shall apply to any grant, contract, or subcontract or other form of financial assistance awarded to or entered into with a contractor/vendor or grantee after the effective date of this Chapter and to the extension or renewal after the effective date of this Chapter of any grant, contract, or subcontract or other form of financial assistance with a contractor/vendor or grantee.

1:815.  Living Wages Required.

(1)	Every contractor/vendor or grantee, as defined in Section 1:813, shall pay its covered employees a living wage as established in this Section.

(a)	For a covered employer that provides employee health care to its employees, the living wage shall be $8.70 an hour, or the adjusted amount hereafter established under Section 1:815(3).

(b)	For a covered employer that does not provide health care to its employees, the living wage shall be $10.20 a hour, or the adjusted amount hereafter established under Section 1:815(3).

(2)	In order to qualify to pay the living wage rate for covered employers providing employee health care under subsection 1:815(1)(a), a covered employer shall furnish proof of said health care coverage and payment therefor to the City Administrator or his/her designee.

(3)	The amount of the living wage established in this Section shall be adjusted upward no later than April 30, 2002, and every year thereafter by a percentage equal to the percentage increase, if any, in the federal poverty guidelines as published by the United States Department of Health and Human Services for the years 2001 and 2002.  Subsequent annual adjustments shall be based upon the percentage increase, if any, in the United States Department of Health and Human Services poverty guidelines when comparing the prior calendar year's poverty guidelines to the present calendar year's guidelines.  The applicable percentage amount will be converted to an amount in cents by multiplying the existing wage under Section 1.815(1)(b) by said percentage, rounding upward to the next cent, and adding this amount of cents to the existing living wage levels established under Sections 1:815(1)(a) and 1:815(1)(b).  Prior to April 1 of each calendar year, the City will notify any covered employer of this adjustment by posting a written notice in a prominent place in City Hall, and, in the case of a covered employer that has provided an address of record to the City, by a written letter to each such covered employer.

Section 5 - Non-Discrimination

The Contractor agrees to comply with the nondiscrimination provisions of Chapter 112 of the Ann Arbor City Code and to take affirmative action to assure that applicants are employed and that employees are treated during employment in a manner which provides equal employment opportunity and tends to eliminate any inequality based upon race, national origin or sex.  The Contractor agrees to comply with the provisions of Section 9:161 of Chapter 112 of the Ann Arbor City Code and in particular the following excerpts:

9:161	NONDISCRIMINATION BY CITY CONTRACTORS

(1)	All contractors proposing to do business with the City of Ann Arbor shall satisfy the nondiscrimination administrative policy adopted by the City Administrator in accordance with the guidelines of this section. All contractors shall receive approval from the Director prior to entering into a contract with the City, unless specifically exempted by administrative policy.  All City contractors shall take affirmative action to insure that applicants are employed and that employees are treated during employment in a manner which provides equal employment opportunity and tends to eliminate inequality based upon race, national origin or sex.

(2)	Each prospective contractor shall submit to the City data showing current total employment by occupational category, sex and minority group.  If, after verifying this data, the Director concludes that it indicates total minority and female employment commensurate with their availability within the contractor's labor recruitment area, i.e., the area from which the contractor can reasonably be expected to recruit, said contractor shall be accepted by the Director as having fulfilled affirmative action requirements for a period of one year at which time the Director shall conduct another review.  Other contractors shall develop an affirmative action program in conjunction with the Director.  Said program shall include specific goals and timetables for the hiring and promotion of minorities and females.  Said goals shall reflect the availability of minorities and females within the contractor's labor recruitment area.  In the case of construction contractors, the Director shall use for employment verification the labor recruitment area of the Ann Arbor-Ypsilanti standard metropolitan statistical area. Construction contractors determined to be in compliance shall be accepted by the Director as having fulfilled affirmative action requirements for a period of six (6) months at which time the Director shall conduct another review.

(3)	In hiring for construction projects, contractors shall make good faith efforts to employ local persons, so as to enhance the local economy.

(4)	All contracts shall include provisions through which the contractor agrees, in addition to any other applicable Federal or State labor laws:

(a)	To set goals, in conference with the Human Resources Director, for each job category or division of the work force used in the completion of the City work;

(b)	To provide periodic reports concerning the progress the contractor has made in meeting the affirmative action goals it has agreed to;

(c)	To permit the Director access to all books, records and accounts pertaining to its employment practices for the purpose of determining compliance with the affirmative action requirements.

(5)	The Director shall monitor the compliance of each contractor with the nondiscrimination provisions of each contract.  The Director shall develop procedures and regulations consistent with the administrative policy adopted by the City Administrator for notice and enforcement of non-compliance. Such procedures and regulations shall include a provision for the posting of contractors not in compliance.

(6)	All City contracts shall provide further that breach of the obligation not to discriminate shall be a material breach of the contract for which the City shall be entitled, at its option, to do any or all of the following:

(a)	To cancel, terminate, or suspend the contract in whole or part and/or refuse to make any required periodic payments under the contract;

(b)	Declare the contractor ineligible for the award of any future contracts with the City for a specified length of time;

(c)	To recover liquidated damages of a specified sum, said sum to be that percentage of the labor expenditure for the time period involved which would have accrued to minority group members had the affirmative action not been breached;

(d)	Impose for each day of non-compliance, liquidated damages of a specified sum, based upon the following schedule:

| Contract Amount | Assessed Damages Per Day of Non-Compliance |
| --- | --- |
| $ 10,000 - 24,999 25,000 - 99,999 100,000 - 199,999 200,000 - 499,999 500,000 - 1,499,999 1,500,000 - 2,999,999 3,000,000 - 4,999,999 5,000,000 - and above | $ 25.00 50.00 100.00 150.00 200.00 250.00 300.00 500.00 |

(e)	In addition the contractor shall be liable for any costs or expenses incurred by the City of Ann Arbor in obtaining from other sources the work and services to be rendered or performed or the goods or properties to be furnished or delivered to the City under this contract.

Section 6 - Materials, Appliances, Employees

Unless otherwise stipulated, the Contractor shall provide and pay for all materials, labor, water, tools, equipment, light, power, transportation, and other facilities necessary or used for the execution and completion of the work. Unless otherwise specified, all materials incorporated in the permanent work shall be new, and both workmanship and materials shall be of the highest quality. The Contractor shall, if required, furnish satisfactory evidence as to the kind and quality of materials.

The Contractor shall at all times enforce strict discipline and good order among its employees, and shall seek to avoid employing on the work any unfit person or anyone not skilled in the work assigned.

Adequate sanitary facilities shall be provided by the Contractor.

Section 7 - Qualifications for Employment

The Contractor shall employ competent laborers and mechanics for the work under this Contract.  For work performed under this Contract, employment preference shall be given  to qualified local residents.

Section 8 - Royalties and Patents

The Contractor shall pay all royalties and license fees. It shall defend all suits or claims for infringements of any patent rights and shall hold the City harmless from loss on account of infringement except that the City shall be responsible for all infringement loss when a particular process or the product of a particular manufacturer or manufacturers is specified, unless the City has notified the Contractor prior to the signing of the Contract that the particular process or product is patented or is believed to be patented.

Section 9 - Permits and Regulations

The Contractor must secure and pay for all permits, permit or plan review fees and licenses necessary for the prosecution of the work. These include but are not limited to City building permits, right-of-way permits, lane closure permits, right-of-way occupancy permits, and the like. The City shall secure and pay for easements shown on the plans unless otherwise specified.

The Contractor shall give all notices and comply with all laws, ordinances, rules and regulations bearing on the conduct of the work as drawn and specified. If the Contractor observes that the contract documents are at variance with those requirements, it shall promptly notify the Supervising Professional in writing, and any necessary changes shall be adjusted as provided in the Contract for changes in the work.

Section 10 - Protection of the Public and of Work and Property

The Contractor is responsible for the means, methods, sequences, techniques and procedures of construction and safety programs associated with the work contemplated by this contract. The Contractor, its agents or sub-contractors, shall comply with the "General Rules and Regulations for the Construction Industry" as published by the Construction Safety Commission of the State of Michigan and to all other local, State and National laws, ordinances, rules and regulations pertaining to safety of persons and property.

The Contractor shall take all necessary and reasonable precautions to protect the safety of the public.  It shall continuously maintain adequate protection of all work from damage, and shall take all necessary and reasonable precautions to adequately protect all public and private property from injury or loss arising in connection with this Contract. It shall make good any damage, injury or loss to it's work and to public and private property resulting from lack of reasonable protective precautions, except as may be due to errors in the contract documents, or caused by agents or employees of the City. The Contractor shall obtain and maintain sufficient insurance to cover damage to any City property at the site by any cause.

In an emergency affecting the safety of life, or the work, or of adjoining property, the Contractor is, without special instructions or authorization from the Supervising Professional, permitted to act at its discretion to prevent the threatened loss or injury.  It shall also so act, without appeal, if authorized or instructed by the Supervising Professional.

Any compensation claimed by the Contractor for emergency work shall be determined by agreement or in accordance with the terms of Claims for Extra Cost - Section 15.

Section 11 - Inspection of Work

The City shall provide sufficient competent personnel for the inspection of the work.

The Supervising Professional shall at all times have access to the work whenever it is in preparation or progress, and the Contractor shall provide proper facilities for access and for inspection.

If the specifications, the Supervising Professional's instructions, laws, ordinances, or any public authority require any work to be specially tested or approved, the Contractor shall give the Supervising Professional timely notice of its readiness for inspection, and if the inspection is by an authority other than the Supervising Professional, of the date fixed for the inspection. Inspections by the Supervising Professional shall be made promptly, and where practicable at the source of supply. If any work should be covered up without approval or consent of the Supervising Professional, it must, if required by the Supervising Professional, be uncovered for examination and properly restored at the Contractor's expense.

Re-examination of any work may be ordered by the Supervising Professional, and, if so ordered, the work must be uncovered by the Contractor. If the work is found to be in accordance with the contract documents, the City shall pay the cost of re-examination and replacement. If the work is not in accordance with the contract documents, the Contractor shall pay the cost.

Section 12 - Superintendence

The Contractor shall keep on the work site, during its progress, a competent superintendent and any necessary assistants, all satisfactory to the Supervising Professional. The superintendent will be responsible to perform all on-site project management for the Contractor. The superintendent shall be experienced in the work required for this Contract. The superintendent shall represent the Contractor and all direction given to the superintendent shall be binding as if given to the Contractor. Important directions shall immediately be confirmed in writing to the Contractor.  Other directions will be confirmed on written request. The Contractor shall give efficient superintendence to the work, using its best skill and attention.

Section 13 - Changes in the Work

The City may make changes to the quantities of work within the general scope of the Contract at any time by a written order and without notice to the sureties. If the changes add to or deduct from the extent of the work, the Contract Sum shall be adjusted accordingly. All the changes shall be executed under the conditions of the original Contract except that any claim for extension of time caused by the change shall be adjusted at the time of ordering the change.

In giving instructions, the Supervising Professional shall have authority to make minor changes in the work not involving extra cost and not inconsistent with the purposes of the work, but otherwise, except in an emergency endangering life or property, no extra work or change shall be made unless in pursuance of a written order by the Supervising Professional, and no claim for an addition to the Contract Sum shall be valid unless the additional work was ordered in writing.

The Contractor shall proceed with the work as changed and the value of the work shall be determined as provided in Claims for Extra Cost - Section 15.

Section 14 - Extension of Time

Extension of time stipulated in the Contract for completion of the work will be made if and as the Supervising Professional may deem proper under any of the following circumstances:

(1)	When work under an extra work order is added to the work under this Contract;

(2)	When the work is suspended as provided in Section 20;

(3)	When the work of the Contractor is delayed on account of conditions which could not have been foreseen, or which were beyond the control of the Contractor, and which were not the result of its fault or negligence;

(4)	Delays in the progress of the work caused by any act or neglect of the City or of its employees or by other Contractors employed by the City;

(5)	Delay due to an act of Government;

(6)	Delay by the Supervising Professional in the furnishing of plans and necessary information;

(7)	Other cause which in the opinion of the Supervising Professional entitles the Contractor to an extension of time.

The Contractor shall notify the Supervising Professional within 7 days of an occurrence or conditions which, in the Contractor's opinion, entitle it to an extension of time. The notice shall be in writing and submitted in ample time to permit full investigation and evaluation of the Contractor's claim. The Supervising Professional shall acknowledge receipt of the Contractor's notice within 7 days of its receipt. Failure to timely provide the written notice shall constitute a waiver by the Contractor of any claim.

In situations where an extension of time in contract completion is appropriate under this or any other section of the contract, the Contractor understands and agrees that the only available adjustment for events that cause any delays in contract completion shall be extension of the required time for contract completion and that there shall be no adjustments in the money due the Contractor on account of the delay.

Section 15 - Claims for Extra Cost

If the Contractor claims that any instructions by drawings or other media issued after the date of the Contract involved extra cost under this Contract, it shall give the Supervising Professional written notice within 7 days after the receipt of the instructions, and in any event before proceeding to execute the work, except in emergency endangering life or property. The procedure shall then be as provided for Changes in the Work-Section l3. No claim shall be valid unless so made.

If the Supervising Professional orders, in writing, the performance of any work not covered by the contract documents, and for which no item of work is provided in the Contract, and for which no unit price or lump sum basis can be agreed upon, then the extra work shall be done on a Cost-Plus-Percentage basis of payment as follows:

(1)	The Contractor shall be reimbursed for all reasonable costs incurred in doing the work, and shall receive an additional payment of 15% of all the reasonable costs to cover both its indirect overhead costs and profit;

(2)	The term "Cost" shall cover all payroll charges for employees and supervision required under the specific order, together with all worker's compensation, Social Security, pension and retirement allowances and social insurance, or other regular payroll charges on same; the cost of all material and supplies required of either temporary or permanent character; rental of all power-driven equipment at agreed upon rates, together with cost of fuel and supply charges for the equipment; and any costs incurred by the Contractor as a direct result of executing the order, if approved by the Supervising Professional;

(3)	If the extra is performed under subcontract, the subcontractor shall be allowed to compute its charges as described above. The Contractor shall be permitted to add an additional charge of 5% percent to that of the subcontractor for the Contractor's supervision and contractual responsibility;

(4)	The quantities and items of work done each day shall be submitted to the Supervising Professional in a satisfactory form on the succeeding day, and shall be approved by the Supervising Professional and the Contractor or adjusted at once;

(5)	Payments of all charges for work under this Section in any one month shall be made along with normal progress payments. Retainage shall be in accordance with Progress Payments-Section 16.

No additional compensation will be provided for additional equipment, materials, personnel, overtime or special charges required to perform the work within the time requirements of the Contract.

When extra work is required and no suitable price for machinery and equipment can be determined in accordance with this Section, the hourly rate paid shall be 1/40 of the basic weekly rate listed in the Rental Rate Blue Book published by Dataquest Incorporated and applicable to the time period the equipment was first used for the extra work. The hourly rate will be deemed to include all costs of operation such as bucket or blade, fuel, maintenance, "regional factors", insurance, taxes, and the like, but not the costs of the operator.

Section 16 - Progress Payments

The Contractor shall submit each month, or at longer intervals, if it so desires, an invoice covering work performed for which it believes payment, under the Contract terms, is due. The submission shall be to the City's Finance Department - Accounting Division.  The Supervising Professional will, within 10 days following submission of the invoice, prepare a certificate for payment for the work in an amount to be determined by the Supervising Professional as fairly representing the acceptable work performed during the period covered by the Contractor's invoice. To insure the proper performance of this Contract, the City will retain a percentage of the estimate in accordance with Act 524, Public Acts of 1980. The City will then, following the receipt of the Supervising Professional's Certificate, make payment to the Contractor as soon as feasible, which is anticipated will be within 15 days.

An allowance may be made in progress payments if substantial quantities of permanent material have been delivered to the site but not incorporated in the completed work if the Contractor, in the opinion of the Supervising Professional, is diligently pursuing the work under this Contract. Such materials shall be properly stored and adequately protected. Allowance in the estimate shall be at the invoice price value of the items. Notwithstanding any payment of any allowance, all risk of loss due to vandalism or any damages to the stored materials remains with the Contractor.

In the case of Contracts which include only the Furnishing and Delivering of Equipment, the payments shall be; 60% of the Contract Sum upon the delivery of all equipment to be furnished, or in the case of delivery of a usable portion of the equipment in advance of the total equipment delivery, 60% of the estimated value of the portion of the equipment may be paid upon its delivery in advance of the time of the remainder of the equipment to be furnished; 30%  of the Contract Sum upon completion of erection of all equipment furnished, but not later than 60 days after the date of delivery of all of the equipment to be furnished; and payment of the final 10% on final completion of erection, testing and acceptance of all the equipment to be furnished; but not later than l80 days after the date of delivery of all of the equipment to be furnished, unless testing has been completed and shows the equipment to be unacceptable.

With each invoice for periodic payment, the Contractor shall enclose a Contractor's Declaration - Section 43, and an updated project schedule per Order of Completion - Section 2.

Section 17 - Deductions for Uncorrected Work

If the Supervising Professional decides it is inexpedient to correct work that has been damaged or that was not done in accordance with the Contract, an equitable deduction from the Contract price shall be made.

Section 18 - Correction of Work Before Final Payment

The Contractor shall promptly remove from the premises all materials condemned by the Supervising Professional as failing to meet Contract requirements, whether incorporated in the work or not, and the Contractor shall promptly replace and re-execute the work in accordance with the Contract and without expense to the City and shall bear the expense of making good all work of other contractors destroyed or damaged by the removal or replacement.

If the Contractor does not remove the condemned work and materials within l0 days after written notice, the City may remove them and, if the removed material has value, may store the material at the expense of the Contractor. If the Contractor does not pay the expense of the removal within 10 days thereafter, the City may, upon 10 days written notice, sell the removed materials at auction or private sale and shall pay to the Contractor the net proceeds, after deducting all costs and expenses that should have been borne by the Contractor. If the removed material has no value, the Contractor must pay the City the expenses for disposal within 10 days of invoice for the disposal costs.

The inspection or lack of inspection of any material or work pertaining to this Contract shall not relieve the Contractor of its obligation to fulfill this Contract and defective work shall be made good. Unsuitable materials may be rejected by the Supervising Professional notwithstanding that the work and materials have been previously overlooked by the Supervising Professional and accepted or estimated for payment or paid for. If the work or any part shall be found defective at any time before the final acceptance of the whole work, the Contractor shall forthwith make good the defect in a manner satisfactory to the Supervising Professional. The judgment and the decision of the Supervising Professional as to whether the materials supplied and the work done under this Contract comply with the requirements of the Contract shall be conclusive and final.

Section 19 - Acceptance and Final Payment

Upon receipt of written notice that the work is ready for final inspection and acceptance, the Supervising Professional will promptly make the inspection. When the Supervising Professional finds the work acceptable under the Contract and the Contract fully performed, the Supervising Professional will promptly sign and issue a final certificate stating that the work required by this Contract has been completed and is accepted by the City under the terms and conditions of the Contract. The entire balance found to be due the Contractor, including the retained percentage, shall be paid to the Contractor by the City within 30 days after the date of the final certificate.

Before issuance of final certificates, the Contractor shall file with the City:

(1)	The consent of the surety to payment of the final estimate;

(2)	The Contractor's Affidavit in the form required by Section 44.

In case the Affidavit or consent is not furnished, the City may retain out of any amount due the Contractor, sums sufficient to cover all lienable claims.

The making and acceptance of the final payment shall constitute a waiver of all claims by the City except those arising from:

(1)	unsettled liens;

(2)	faulty work appearing within 12 months after final payment;

(3)	hidden defects in meeting the requirements of the plans and specifications;

(4)	manufacturer's guarantees.

It shall also constitute a waiver of all claims by the Contractor, except those previously made and still unsettled.

Section 20 - Suspension of Work

The City may at any time suspend the work, or any part by giving 5 days notice to the Contractor in writing. The work shall be resumed by the Contractor within 10 days after the date fixed in the written notice from the City to the Contractor to do so. The City shall reimburse the Contractor for expense incurred by the Contractor in connection with the work under this Contract as a result of the suspension.

If the work, or any part, shall be stopped by the notice in writing, and if the City does not give notice in writing to the Contractor to resume work at a date within 90 days of the date fixed in the written notice to suspend, then the Contractor may abandon that portion of the work suspended and will be entitled to the estimates and payments for all work done on the portions abandoned, if any, plus 10% of the value of the work abandoned, to compensate for loss of overhead, plant expense, and anticipated profit.

Section 21 - Delays and The City's Right to Terminate Contract

If the Contractor refuses or fails to prosecute the work, or any separate part of it, with the diligence required to insure completion, ready for operation, within the allowable number of consecutive calendar days specified plus extensions, or fails to complete the work within the required time, the City may, by written notice to the Contractor, terminate its right to proceed with the work or any part of the work as to which there has been delay. After providing the notice the City may take over the work and prosecute it to completion, by contract or otherwise, and the Contractor and its sureties shall be liable to the City for any excess cost to the City. If the Contractor's right to proceed is terminated, the City may take possession of and utilize in completing the work, any materials, appliances and plant as may be on the site of the work and useful for completing the work. The right of the Contractor to proceed shall not be terminated or the Contractor charged with liquidated damages where an extension of time is granted under Extension of Time - Section 14.

If the Contractor is adjudged a bankrupt, or if it makes a general assignment for the benefit of creditors, or if a receiver is appointed on account of its insolvency, or if it persistently or repeatedly refuses or fails except in cases for which extension of time is provided, to supply enough properly skilled workers or proper materials, or if it fails to make prompt payments to subcontractors or for material or labor, or persistently disregards laws, ordinances or the instructions of the Supervising Professional, or otherwise is guilty of a substantial violation of any provision of the Contract, then the City, upon the certificate of the Supervising Professional that sufficient cause exists to justify such action, may, without prejudice to any other right or remedy and after giving the Contractor 3 days written notice, terminate this Contract. The City may then take possession of the premises and of all materials, tools and appliances thereon and without prejudice to any other remedy it may have, make good the deficiencies or finish the work by whatever method it may deem expedient, and deduct the cost from the payment due the Contractor. The Contractor shall not be entitled to receive any further payment until the work is finished. If the expense of finishing the work, including compensation for additional managerial and administrative services exceeds the unpaid balance of the Contract Sum,  the Contractor and its surety are liable to the City for any excess cost incurred. The expense incurred by the City, and the damage incurred through the Contractor's default, shall be certified by the Supervising Professional.

Section 22 - Contractor's Right to Terminate Contract

If the work should be stopped under an order of any court, or other public authority, for a period of 3 months, through no act or fault of the Contractor or of anyone employed by it, then the Contractor may, upon 7 days written notice to the City, terminate this Contract and recover from the City payment for all acceptable work executed plus reasonable profit.

Section 23 - City's Right To Do Work

If the Contractor should neglect to prosecute the work properly or fail to perform any provision of this Contract, the City, 3 days after giving written notice to the Contractor and its surety may, without prejudice to any other remedy the City may have, make good the deficiencies and may deduct the cost from the payment due to the Contractor.

Section 24 - Removal of Equipment and Supplies

In case of termination of this Contract before completion, from any or no cause, the Contractor, if notified to do so by the City, shall promptly remove any part or all of its equipment and supplies from the property of the City, failing which the City shall have the right to remove the equipment and supplies at the expense of the Contractor.

The removed equipment and supplies may be stored by the City and, if all costs of removal and storage are not paid by the Contractor within 10 days of invoicing, the City upon 10 days written notice may sell the equipment and supplies at auction or private sale, and shall pay the Contractor the net proceeds after deducting all costs and expenses that should have been borne by the Contractor and after deducting all amounts claimed due by any lien holder of the equipment or supplies.

Section 25 - Responsibility for Work and Warranties

The Contractor assumes full responsibility for any and all materials and equipment used in the construction of the work and may not make claims against the City for damages to materials and equipment from any cause except negligence or willful act of the City. Until its final acceptance, the Contractor shall be responsible for damage to or destruction of the project (except for any part covered by Partial Completion and Acceptance - Section 26).  The Contractor shall make good all work damaged or destroyed before acceptance. All risk of loss remains with the Contractor until final acceptance of the work (Section 19) or partial acceptance (Section 26).  The Contractor is advised to investigate obtaining its own builders risk insurance.

The Contractor shall guarantee the quality of the work for a period of one year.  The Contractor shall also unconditionally guarantee the quality of all equipment and materials that are furnished and installed under the contract for a period of one year.  At the end of one year after the Contractor's receipt of final payment, the complete work, including equipment and materials furnished and installed under the contract, shall be inspected by the Contractor and the Supervising Professional. Any defects shall be corrected by the Contractor at its expense as soon as practicable but in all cases within 60 days. Any defects that are identified prior to the end of one year shall also be inspected by the Contractor and the Supervising Professional and shall be corrected by the Contractor at its expense as soon as practicable but in all cases within 60 days.

The Contractor shall assign all manufacturer or material supplier warranties to the City prior to final payment. The assignment shall not relieve the Contractor of its obligations under this paragraph to correct defects.

Section 26 - Partial Completion and Acceptance

If at any time prior to the issuance of the final certificate referred to in Acceptance and Final Payment - Section 19, any portion of the permanent construction has been satisfactorily completed, and if the Supervising Professional determines that portion of the permanent construction is not required for the operations of the Contractor but is needed by the City, the Supervising Professional shall issue to the Contractor a certificate of partial completion, and immediately the City may take over and use the portion of the permanent construction described in the certificate, and exclude the Contractor from that portion.

The issuance of a certificate of partial completion shall not constitute an extension of the Contractor's time to complete the portion of the permanent construction to which it relates if the Contractor has failed to complete it in accordance with the terms of this Contract. The issuance of the certificate shall not release the Contractor or its sureties from any obligations under this Contract including bonds.

If prior use increases the cost of, or delays the work, the Contractor shall be entitled to extra compensation, or extension of time, or both, as the Supervising Professional may determine.

Section 27 - Payments Withheld Prior to Final

Acceptance of Work

The City may withhold or, on account of subsequently discovered evidence, nullify the whole or part of any certificate to the extent reasonably appropriate to protect the City from loss on account of:

(1)	Defective work not remedied;

(2)	Claims filed or reasonable evidence indicating probable filing of claims by other parties against the Contractor;

(3)	Failure of the Contractor to make payments properly to subcontractors or for material or labor;

(4)	Damage to another Contractor.

When the above grounds are removed or the Contractor provides a Surety Bond satisfactory to the City which will protect the City in the amount withheld, payment shall be made for amounts withheld under this section.

Section 28 - Contractor's Insurance

A.	The Contractor shall procure and maintain during the life of this Contract, including the guarantee period and during any warranty work, such insurance policies, including those set forth below, as will protect itself from all claims for bodily injuries, death or property damage which may arise under this Contract; whether the acts were made by the Contractor or by any subcontractor or anyone employed by them directly or indirectly.  The following insurance policies are required:

1.	Worker's Compensation Insurance in accordance with all applicable state and federal statutes. Further, Employers Liability Coverage shall be obtained in the following minimum amounts:

Bodily Injury by Accident - $500,000 each accident

Bodily Injury by Disease - $500,000 each employee

Bodily Injury by Disease - $500,000 each policy limit

2.	Commercial General Liability Insurance equivalent to, as a minimum, Insurance Services Office form CG 00 01 07 98. The City of Ann Arbor shall be named as an additional insured. There shall be no added exclusions or limiting endorsements including, but not limited to:   Products and Completed Operations, Explosion, Collapse and Underground coverage or Pollution. Further, the following minimum limits of liability are required:

$1,000,000	Each occurrence as respect Bodily Injury Liability or Property Damage Liability, or both combined.

$2,000,000	Per Job General Aggregate

$1,000,000	Personal and Advertising Injury

$2,000,000	Products and Completed Operations Aggregate

3.	Motor Vehicle Liability Insurance, including Michigan No-Fault Coverages, equivalent to, as a minimum, Insurance Services Office form CA 00 01 07 97. The City of Ann Arbor shall be named as an additional insured. There shall be no added exclusions or limiting endorsements. Coverage shall include all owned vehicles, all non-owned vehicles and all hired vehicles. Further, the limits of liability shall be $1,000,000 for each occurrence as respects Bodily Injury Liability or Property Damage Liability, or both combined.

4.	Umbrella/Excess Liability Insurance shall be provided to apply excess of the Commercial General Liability, Employers Liability and the Motor Vehicle coverage enumerated above, for each occurrence and for aggregate in the amount of $1,000,000.

B.	Insurance required under Section A.2 and A.3 of this Contract shall be considered primary as respects any other valid or collectible insurance that the City may possess, including any self-insured retentions the City may have; and any other insurance the City does possess shall be considered excess insurance only and shall not be required to contribute with this insurance. Further, the Contractor agrees to waive any right of recovery by its insurer against the City.

C.	In the case of all Contracts involving on-site work, the Contractor shall provide to the City before the commencement of any work under this Contract documentation demonstrating it has obtained the above mentioned policies. Documentation must provide and demonstrate an unconditional 30 day written notice of cancellation in favor of the City of Ann Arbor. Further, the documentation must explicitly state the following:  (a) the policy number; name of insurance company; name and address of the agent or authorized representative; name and address of insured; project name; policy expiration date; and specific coverage amounts; (b) any deductibles or self-insured retentions which shall be approved by the City, in its sole discretion; (c) that the policy conforms to the requirements specified. An original certificate of insurance may be provided as an initial indication of the required insurance, provided that no later than 21 calendar days after commencement of any work the Contractor supplies a copy of the endorsements required on the policies. Upon request, the Contractor shall provide within 30 days a copy of the policy(ies) to the City. If any of the above coverages expire by their terms during the term of this Contract, the Contractor shall deliver proof of renewal and/or new policies to the Administering Department at least ten days prior to the expiration date.

D.	Any Insurance provider of Contractor shall be admitted and authorized to do business in the State of Michigan and shall carry and maintain a minimum rating assigned by A.M. Best & Company’s Key Rating Guide of A- Overall and a minimum Financial Size Category of V. Insurance policies and certificates issued by non-admitted insurance companies are not acceptable unless approved in writing by the City.

Section 29 - Surety Bonds

Bonds will be required from the successful bidder as follows:

(1)	A Performance Bond to the City of Ann Arbor for the amount of the bid(s) accepted;

(2)	A Labor and Material Bond to the City of Ann Arbor for the amount of the bid(s) accepted.

Bonds shall be executed on forms supplied by the City in a manner and by a Surety Company satisfactory to the City Attorney.

Section 30 - Damage Claims

The Contractor shall be held responsible for all damages to property of the City or others, caused by or resulting from the negligence of the Contractor, its employees, or agents during the progress of or connected with the prosecution of the work, whether within the limits of the work or elsewhere. The Contractor must restore all property injured including sidewalks, curbing, sodding, pipes, conduit, sewers or other public or private property to not less than its original condition with new work.

Section 31 - Refusal to Obey Instructions

If the Contractor refuses to obey the instructions of the Supervising Professional, the Supervising Professional shall withdraw inspection from the work, and no payments will be made for work performed thereafter nor may work be performed thereafter until the Supervising Professional shall have again authorized the work to proceed.

Section 32 - Assignment

Neither party to the Contract shall assign the Contract without the written consent of the other.  The Contractor may assign any monies due to it to a third party acceptable to the City.

Section 33 - Rights of Various Interests

Whenever work being done by the City's forces or by other contractors is contiguous to work covered by this Contract, the respective rights of the various interests involved shall be established by the Supervising Professional, to secure the completion of the various portions of the work in general harmony.

The Contractor is responsible to coordinate all aspects of the work, including coordination of, and with, utility companies and other contractors whose work impacts this project.

Section 34 - Subcontracts

The Contractor shall not award any work to any subcontractor without prior written approval of the City. The approval will not be given until the Contractor submits to the City a written statement concerning the proposed award to the subcontractor. The statement shall contain all information the City may require.

The Contractor shall be as fully responsible to the City for the acts and omissions of its subcontractors, and of persons either directly or indirectly employed by them, as it is for the acts and omissions of persons directly employed by it.

The Contractor shall cause appropriate provisions to be inserted in all subcontracts relative to the work to bind subcontractors to the Contractor by the terms of the General Conditions and all other contract documents applicable to the work of the subcontractors and to give the Contractor the same power to terminate any subcontract that the City may exercise over the Contractor under any provision of the contract documents.

Nothing contained in the contract documents shall create any contractual relation between any subcontractor and the City.

Section 35 - Supervising Professional's Status

The Supervising Professional has the right to inspect any or all work. The Supervising Professional has authority to stop the work whenever stoppage may be appropriate to insure the proper execution of the Contract. The Supervising Professional has the authority to reject all work and materials which do not conform to the Contract and to decide questions which arise in the execution of the work.

The Supervising Professional shall make all measurements and determinations of quantities. Those  measurements and determinations are final and conclusive between the parties.

Section 36 - Supervising Professional's Decisions

The Supervising Professional shall, within a reasonable time after their presentation to the Supervising Professional, make decisions in writing on all claims of the City or the Contractor and on all other matters relating to the execution and progress of the work or the interpretation of the contract documents.

Section 37 - Storing Materials and Supplies

Materials and supplies may be stored at the site of the work at locations agreeable to the City unless specific exception is listed elsewhere in these documents. Ample way for foot traffic and drainage must be provided, and gutters must, at all times, be kept free from obstruction. Traffic on streets shall be interfered with as little as possible. The Contractor may not enter or occupy with agents, employees, tools, or material any private property without first obtaining written permission from its owner.  A copy of the permission shall be furnished to the Supervising Professional.

Section 38 - Lands for Work

The Contractor shall provide, at its own expense and without liability to the City, any additional land and access that may be required for temporary construction facilities or for storage of materials.

Section 39 - Cleaning Up

The Contractor shall, as directed by the Supervising Professional, remove at its own expense from the City's property and from all public and private property all temporary structures, rubbish and waste materials resulting from its operations unless otherwise specifically approved, in writing, by the Supervising Professional.

Section 40 - Salvage

The Supervising Professional may designate for salvage any materials from existing structures or underground services. Materials so designated remain City property and shall be transported or stored at a location as the Supervising Professional may direct.

Section 41 - Night, Saturday or Sunday Work

No night or Sunday work (without prior written City approval) will be permitted except in the case of an emergency and then only to the extent absolutely necessary. The City may allow night work which, in the opinion of the Supervising Professional, can be satisfactorily performed at night. Night work is any work between 8:00 p.m. and 7:00 a.m. No Saturday work will be permitted unless the Contractor gives the Supervising Professional at least 48 hours but not more than 5 days notice of the Contractor's intention to work the upcoming Saturday.

Section 42 - Sales Taxes

Under State law the City is exempt from the assessment of State Sales Tax on its direct purchases.  Contractors who acquire materials, equipment, supplies, etc. for incorporation in City projects are not likewise exempt.  State Law shall prevail. The Bidder shall familiarize itself with the State Law and prepare its Bid accordingly. No extra payment will be allowed under this Contract for failure of the Contractor to make proper allowance in this bid for taxes it must pay.

Section 43

CONTRACTOR'S DECLARATION

I hereby declare that I have not, during the period                             , 200     , to

, 20     , performed any work, furnished any materials, sustained any loss, damage or delay, or otherwise done anything in addition to the regular items (or executed change orders) set forth in the Contract titled  Superior Dam Painting and Handrail Replacement Project            ,

for which I shall ask, demand, sue for, or claim compensation or extension of time from the City, except as I hereby make claim for additional compensation or extension of time as set forth on the attached itemized statement. I further declare that I have paid all payroll obligations related to this Contract that have become due during the above period and that all invoices related to this Contract received more than 30 days prior to this declaration have been paid in full except as listed below.

There is/is not (Contractor please circle one and strike one as appropriate) an itemized statement attached regarding a request for additional compensation or extension of time.

__________________

Contractor																		Date

By ____________________________

(Signature)

Its ____________________________

(Title of Office)

Past due invoices, if any, are listed below.

Section 44

CONTRACTOR'S AFFIDAVIT

The undersigned Contractor,                                                       , represents that on   ___________________, 20     , it was awarded a contract by the City of Ann Arbor, Michigan to       __                                                                       under the terms and conditions of a Contract titled Superior Dam Painting and Handrail Replacement Project______.  The Contractor represents that all work has now been accomplished and the Contract is complete.

The Contractor warrants and certifies that all of its indebtedness arising by reason of the Contract has been fully paid or satisfactorily secured; and that all claims from subcontractors and others for labor and material used in accomplishing the project, as well as all other claims arising from the performance of the Contract, have been fully paid or satisfactorily settled. The Contractor agrees that, if any claim should hereafter arise, it shall assume responsibility for it immediately upon request to do so by the City of Ann Arbor.

The Contractor, for valuable consideration received, does further waive, release and relinquish any and all claims or right of lien which the Contractor now has or may acquire upon the subject premises for labor and material used in the project owned by the City of Ann Arbor.

This affidavit is freely and voluntarily given with full knowledge of the facts.

Contractor

By __________________________________________

(Signature)

Its __________________________________________

(Title of Office)

Subscribed and sworn to before me, on this           day of                     , 200____,                          ______________________County, Michigan

Notary Public

My commission expires on:  ________________________________

Supplemental Insurance Requirements

The following supplemental insurance requirements are in addition to those insurance requirements specified in “Section 28 - Contractor’s Insurance” of the General Conditions.

Longshoremen’s and Harbor Worker’s Act Coverage

If applicable, the Contractor shall provide Longshoremen’s and Harbor Worker’s Act coverage and the Maritime Liability exclusion shall be deleted.

Deductible

Contractor shall have self-insured retention or deductible no greater than $25,000 for Commercial General Liability and Motor Vehicle Liability Insurance.

STANDARD SPECIFICATIONS

All work under this contract shall be performed in accordance with the Public Services Department Standard Specifications in effect at the date of availability of the contract documents stipulated in the Advertisement. All work under this Contract which is not included in these Standard Specifications, or which is performed using modifications to these Standard Specifications, shall be performed in accordance with the Detailed Specifications included in these contract documents.

A copy of the Public Services Department Standard Specifications may be purchased from the Engineering Division, (Fourth Floor, City Hall, Ann Arbor, Michigan), for $38.00 per copy.  In addition, a copy of these Standard Specifications is available for public viewing at the Engineering Division office, for review Monday through Friday between the hours of 8:30 a.m. and 4:00 p.m.

#### Section 01000

#### GENERAL REQUIREMENTS

1.0	          DESCRIPTION OF THE WORK

The work to be done as part of this project includes: replacement of approximately 650 LF of handrail; placement of approximately 40 LF of new handrail; replacement of machinery cover and base; replacement of sluice gate side seals and bottom seals (materials provided by Owner); replacement of hoist chains (materials provided by Owner) and related work; preparation and painting of dam walkway support beams, spillway gates, gate arms, trunnion hub, hoist shaft, hoist bearing cover and bearing stand, chain guard, clamp angles and clamp bars, and all related work. Work includes installation of additional fall protection equipment (materials provided by Owner).  All work under this contract shall take place at the Superior Dam and Hydroelectric Plant (FERC #31_52), 6000 First Street, Ypsilanti, MI, 48198.  All work associated with this project shall be completed in 2008.

- TEMPORARY FACILITIES AND SITE RESTORATION

A.	Contractor shall obtain approval of the intended placement location from the Owner prior to erection of any temporary building or utilities. The Contractor shall provide temporary sanitary facilities for the use of their employees.  At the completion of the project, the Contractor shall remove all temporary facilities from the site and restore the area to a condition that is equal to or better than the original .

B.	The Contractor shall make every effort to maintain the project site and work area in a clean and tidy condition.  Refuse shall be cleaned up daily and prevented from having opportunity to enter the river.

- PROTECTION OF PROPERTY AND SAFETY

A.	During the progress of the work, the Contractor shall continuously maintain adequate facilities for the protection and safety of all persons and property.  Any damages or interruptions which do occur to a property, structure, or facility as a result of the Contractor’s acts of commission or  omission shall be remedied at the Contractor’s own expense, including all premium wages, if any, required to remedy such damages or interruptions in the shortest possible time and to the satisfaction of the Owner.

B.	The Contractor shall be responsible at all times for maintaining the work site and project area clean and free of loose debris or materials that could potentially blow into the Huron River.

C.	All the electronic and other equipment located in the vicinity of work area must be covered with two (2) layers of plastic sheeting of 4-mil thickness prior to beginning work.

D.	Contractor shall comply with all applicable OSHA and MIOSHA standards in the course of completing the work included with this contract.

4.0	   FIRE PROTECTION

During mixing and application of paint all flames and smoking shall be prohibited in the vicinity.  The Contractor shall provide his/her own fire protection facilities as required by all applicable codes, and insurance requirements, and shall be fully responsible for maintaining complete fire protection for his/her work, as approved by the Engineer.

- SECURITY AND  ACCESS

The Superior Dam is a limited access facility.  The Contractor must comply with the City of Ann Arbor Water Treatment Plant’s operational provisions for security including, but not limited to:

Provide proper identification of employees.

Employees must have employer issued picture identification on their person at all times.

Provide a list of personnel and vehicles on site.

Notify the plant in advance of material deliveries to the site, including delivery contents.

Contractor shall provide a lock in series with the Owner’s lock (“daisy-chain”) on chains at all access gates.  Gates shall remain locked at all times with exception of entering or exiting the site.

These procedures may be revised by City at any time, as needed.

- MATERIALS, STORAGE AND DISPOSAL

- All materials furnished by the Contractor shall be delivered and distributed at the site by the Contractor.

- Burning or burying on the Site of any material is not permitted.

- The sand-blasted material is to be disposed of in accordance with the Natural Resources and Environmental Protection Act, 1994 PA 451, Parts 31, 55, 111, 115 and 201.  No separate payment for disposal shall be made and the cost of this work is to be included in the painting work.  The Contractor shall furnish to the Owner a certificate of disposal of this material at an appropriate disposal facility, issued by the office of the receiving disposal facility.

- On site handling and storage of flammable liquids and all other toxic or dangerous chemicals shall comply with all safety regulations and codes pertaining thereto.

- Storage method and location shall be subject to approval by the Owner.

- The Contractor’s responsibility for material furnished by the Owner shall begin at the point of delivery thereof to the Contractor.  Material on the site shall become the Contractor’s responsibility on the day of his/her receipt of a fully executed Contract.  The Contractor shall examine all material furnished by the Owner at the time and place of delivery to him/her and shall reject all defective material immediately.  Any material furnished by the Owner and installed by the Contractor without discovery of such defects will, if found defective prior to final acceptance of the work, be replaced with sound material by the Owner.  The Contractor, however, shall, at his/her own expense, furnish all materials, equipment, tools and labor necessary to remove said defective material and install the sound material in a manner satisfactory to the Owner.  Any material furnished by the Owner that becomes damaged after acceptance by the Contractor shall be replaced by the Contractor at his/her own expense.

7.0		WORK SCHEDULE

A.	The work schedule shall be arranged and coordinated with the Owner so as not to interfere with the operations of the dam for a proper control of the flow across the dam.  The work associated with the gate will be taken to be complete only after the successful operation of the gate (opening and closing as mentioned in detailed specifications) and after replacing the hoist chains.  Prior to replacing the hoist chains all other work to be done on the gate shall be finished to the Owner’s satisfaction.

B.	All work associated on the gate shall be conducted during a period of low flow in the Huron River.  Work shall begin no earlier than July 1, 2008 unless so authorized by Owner and shall be completed prior to August 15, 2008.  However, the start of work may be delayed by the Owner if flow in the river makes operation of the dam not possible without the sluiceway in service.

C.	The following sequence of construction activities is provided to the Contractor as rough guidance to the expected order of completion of the incorporated work items:

1.	Replacement of stop log seals.

2.	Installation of stop logs.

3.	Removal of existing gate side seals and bottom seals.

4.	Painting operations, including preparation of painted surfaces.

5.	Replacement of gate seals.

6.	Removal and replacement of hoist chains.

7.	Testing of gate operation.

8.	Removal of stop logs.

Items of work not specifically mentioned above may be completed separately or concurrently with work associated with the gate.

8.0		HOURS OF WORK	 AND HOLIDAYS

The hours of work are weekdays, Monday through Friday, between the hours or 7:00 AM – 8:00 PM.  The Contractor shall work ONLY when there is adequate daylight.  No work shall be conducted on days that are designated City holidays.  For the purpose of this Contract, designated City holidays shall be defined as Memorial Day, Independence Day, Labor Day, Veteran’s Day, Thanksgiving Day, the Friday following Thanksgiving Day, noon to close-of-business on December 24, Christmas Day and noon to close-of-business on December 31.  The Contractor shall not be entitled to any additional compensation or an extension of Contract days for designated City holidays.

9.0		LIQUIDATED DAMAGES

A.	Liquidated damages will be applied independently for each area of improvements that are not completed by the dates set by this Contract.

B.	Where the schedule requirements identified in Detailed Specification Section 01000 Paragraph 6.0, B are not met; including repairs not fully complete, final cleaning, equipment reinstallation and all other work to make the dam’s operable sluiceway gate suitable for Owner operation, non-quantifiable liquidated damages in the following amounts will be applied:

1.	Painting, gate seal replacement and hoist chain replacement:  Liquidated damages in the amount of $500.00 per day will be imposed for each calendar day beyond 45 calendar days after sluice gate is taken out of service that this work is not complete.

2.	Handrail (new and replacement), replacement of machine cover and base, installation of fall protection equipment, and all related work:  Liquidated damages as in the amount of $500.00 per day will be imposed for each calendar day beyond 120 calendar days after the notice to proceed is issued that the work is not complete.

C.	Additional liquidated damages, reflecting actual damages to the dam, and its ability to effectively maintain flow in the Huron River may also be applied at the discretion of the Owner per the Contract Documents.

10.0  	GUARANTEE

A.	The Contractor shall guarantee that all equipment and materials delivered under the Contract and incorporated into the Work will be made from materials suitable and adequate for the purposes intended as described in the Contract, in a workmanlike manner in accordance with the best engineering practice, and that such equipment and materials comply with the Specifications in every respect.  When requested, the Contractor shall be required to submit manufacturer’s drawing and performance data and any independent laboratory test results that may be required to assure product or material conformance with the Specifications.

- The Contractor shall guarantee all work for a period of one year from final acceptance of the project.  All manufacturers’ warranties shall be in the City’s name.

- GOODWILL

The Contractor shall at all times conduct his work in a manner such that disturbance to the surrounding community will be minimum.  Such action shall consist of proper dust, noise, traffic, erosion and site sedimentation control.

- DUST AND SAND CONTROL

A.	The Contractor shall provide, operate and maintain an adequate means of dust control, by providing a barrier to control the spreading of sand, dust, sand-blasting media and paint either in the river or to the surrounding area so as not to disturb the people living in the area around the work site or the vehicular and other traffic in the vicinity of work site.  Contractor shall prevent any material –sand, dust and paint, etc. – from entering the river by the use of a fully enclosed work space.

B.	Should the Contractor be negligent of his/her duties in providing adequate and acceptable dust and debris control, the Owner may, with or without notice, order the Contractor to stop work, or may cause the same to be done and deduct the cost of such work from any monies due or to become due the Contractor under this Contract.  The performance of such work by the Owner, or at his/her insistence, shall service in no way to release the Contractor from his/her liability for dust and debris control.

- MAINTENANCE OF RIVER FLOW

To undertake the work associated with the gate, the flow of the Huron River passing through the gate is to be stopped by means of stop-logs.  In order to maintain dam/river flow at the desired rate, the Contractor shall coordinate with the Owner his/her planning to undertake the work related with the dam.  The Contractor shall be very specific regarding the dates of start of work and finish of work for the gate and shall follow the finalized schedule so that the Owner can plan about regulating the river flow across all of the City’s dams, keeping in view the prevalent general weather conditions at the time of the execution of the work specified under this contract.  The Owner’s permit for said project is to maintain run-of-river.  The Owner is not capable of modulating pond or tail-water elevations at the project for purposes of the work under this Contract.

14.0	SUBMITTALS

Where called for in subsequent sections of the Specifications, shop drawings shall be prepared and submitted to the Owner for review and approval.  The Owner requires that two (2) copies of shop drawings shall be submitted for each item requiring submittal.  Additional copies may be submitted for return to the Contractor for his/her files.  Submitted shop drawings shall be numbered according to specification section, each submitted item shall be identifiable by a number assigned to each item, and each submittal on a single item shall have a number assigned.  The resulting submittal number shall follow the format 05500 (specification section) - 12 (item number) - 1(number of times item has been submitted).  The Contractor shall submit to the Owner shop drawings for all Contractor supplied materials, whether or not specifically called for in subsequent Specification sections.  The Contractor shall not be entitled to additional compensation for the production of shop drawings.  Shop drawings may include, but may not be limited to, product catalog cut-sheets, product samples and/or fabrication design drawings.

15.0	PERMITS

The Owner is responsible for obtaining the permit from Michigan Department of Environmental Quality and the United States Army Corp of Engineers (MDEQ/USACE) for the sand blasting and painting work over the waters of the Huron River.  The Contractor is responsible for adhering to the requirements of the MDEQ/USACE Joint Permit for the protection of the waterway.

16.0	FINAL ACCEPTANCE OF THE PROJECT

The project shall be taken as completed in its entirety only when the stop-logs have been transported back to Barton Pump Station from Superior Dam and stored in the same position, the way they are stored at the start of the work.  The return of the stop-logs to their storage location shall not be allowed until the work of replacing and calibrating of hoist chains and leak testing of the replacement gate seals has been completed to the Owner’s satisfaction.  Contractor shall note that the only successful leak testing result shall be no visible leakage.

- METHOD OF MEASUREMENT AND BASIS OF PAYMENT

- Painting of sluice gate components:  Measurement for this item is Lump-Sum.  The price includes the cost of materials, labor, tools and equipment required for painting work, erection and maintenance of containment equipment, and disposal of sand-blasted material.  This price also includes the cost of all equipment and labor required to transport the stop-logs from Barton Pump Station, modify and place the stop-logs in position at Superior Dam, and to transport back the stop-logs from Superior Dam to Barton Pump Station.

- Replacement of Seals and Hoist Chains:  Measurement for this item is Lump-Sum.  The price includes the cost of all equipment and labor required to remove the existing seals, drilling holes for bolts in new seals, placing the new seals in their proper position per the details, removing the existing hoist chains and replacing with new chains and connecting hardware, and greasing the new chains.

- Replacement of Handrails:  Measurement for this item is Lump-Sum.  The price includes the cost of materials, labor, tools and equipment necessary for the removal of existing handrail and the placement of new handrail.  This price also includes costs associated with the production of shop drawings for the replacement handrail and proper disposal of existing handrail.

- Installation of fall protection equipment:  Measurement for this item is Lump-Sum.  The price includes the cost of materials, labor, tools and equipment necessary for the installation of fall protection equipment furnished by the Owner on existing concrete structures at Superior Dam.

- Replacement of Machinery Cover and Base:  Measurement for this item is Lump-Sum.  The price includes the cost of all materials, labor, equipment and tools required to fabricate and install the replacement machinery cover and base as detailed on the plans and specifications.  This price also includes any costs associated with removal and disposal of existing machinery cover and base, and production of shop drawings prepared and sealed by a Professional Engineer licensed by the State of Michigan.

- Painting of dam walkway structural steel:  Measurement for this item is Lump-Sum.  The price includes the cost of materials, labor, tools and equipment required for painting work, erection and maintenance of containment equipment, and disposal of sand-blasted material.  This price also includes costs associated with the removal, storage and replacement of the dam walkway.

END OF SECTION

Section 05500

METAL FABRICATIONS

## PART 1	GENERAL

This specification covers fabrication and replacement of handrails, replacement of machinery cover and base, removal and replacement of hoist chains, and replacement of existing hardware used to fasten and attached any removed, replaced or new metal items.

  - REFERENCES

- ASTM A36-05 Specification for Carbon Structural Steel

- ASTM A307 Specification for Carbon Steel Bolts and Studs

- ASTM A563 Specification for Carbon and Alloy Steel Nuts

- ASTM A 6 – Weld ability

- ASTM A992-06a – Standard specification for structural steel shapes.

- ASTM F1554-07a – Standard specification for anchor bolts, steel, 36, 55 and 105-ksi yield strength.

- ASTM A505-00 (2005) – Standard specifications for steel, sheet and strip, alloy, hot-rolled and cold-rolled, general requirements for.

- ASTM A780-01 (2006) – Standard practice for repair of damaged and uncoated areas of hot-dipped galvanized coatings.

- ASTM A384-07 – Standard practice for safeguarding against warping and distortion during hot-dipping galvanizing of steel assemblies.

- ASTM A123-02 – Standard specification for zinc (hot-dip galvanized) coatings on iron and steel products.

- ASTM A446 – Specification for the Physical Quality of Zinc-Coated (Galvanized) Steel Sheet by the Hot-Dip Process.

1.2	STANDARDS

Handrails shall comply with the Michigan Occupational Safety and Health Act Standards and all federal and/or local safety standards as they apply for general hazards regarding falling.

##### PART 2	PRODUCTS

  - MACHINERY COVER AND BASE

Fabricate to dimensions of the attached drawing.  Construct of hot-dipped galvanized carbon steel to match existing cover and base’s thickness in accordance with ASTM A36-05.  Galvanizing shall be in accordance with ASTM A123.  Modifications of the original machinery cover design have been incorporated into the attached drawing.

2.2	HANDRAIL

- Construct pipe railing of standard, Schedule 40 wrought steel pipe complying with ASTM A120 or ASTM A501 standards.  Unless indicated to the contrary on the Drawings, use nominal 1-1/2” diameter pipe for rails and posts.  All handrail shall be hot-dipped galvanized in accordance with ASTM A123.  Pipe railing is required for handrails, and standard barriers.  Where used as handrails and standard barrier, the vertical distance from the floor to the upper surface of the top rail shall be 42 inches.  Where changes in height of the railings are required, provide a smooth transition without discontinuity in the railing.  Provide pipe railing assemblies with intermediate railings or expanded metal panels as indicated on the Drawings.

- Provide and install pipe railing assemblies strong enough to withstand a 300 lb horizontal force at the railing's weakest point.  Deflection of top rail by horizontal force shall not exceed ¼”.  Space posts not more than 6 ft apart.

- Weld and grind smooth all joints.  Repair any damage to galvanized finish with cold galvanizing paint.  Use special fittings where non-perpendicular joints occur.  Anchor railing posts to concrete with epoxy set anchors.  Set railings to line and elevation and brace until all posts are securely anchored.  Anchor railings to structural steel framing by welding.  Anchor railings to masonry by anchor bolting.

2.3	GUARD CHAINS

Provide 3/16” nickel-chrome link construction guard chains where indicated on the Drawings.  Supply chains with snap-type fasteners at teach end to permit attachment to standard eyelets.

2.4	HOIST CHAINS

A.		Replacement hoist chains, shackles and U-bolts shall be furnished by the City of Ann Arbor.  Grease for chain lubrication after installation shall be furnished by the City of Ann Arbor.

B.		The Contractor shall submit his/her proposed sequence of construction for this portion of the work for the Owner’s review and approval.

2.5	FALL PROTECTION EQUIPMENT

Fall protection equipment shall be furnished by the City of Ann Arbor.  Catalog cut sheets for the equipment to be installed are provided in Appendix B of the Contract Document.

2.6	ANCHORS

- All anchors shall be Hilti-HIT-HY 150 Epoxy Injection System with stainless steel anchors, bolts or threaded rod.

- Install all anchors in strict accordance with manufacturer's recommendations.

2.7 	BOLTS AND SCREWS

The Contractor shall salvage existing bolts and screws wherever possible for reuse on replacement items.  Whenever existing bolts and screws are not salvageable, the Contractor shall replace the bolts and screws with stainless steel of the same size and type as those removed by the Contractor.

  - WELDS

Produce welds in accordance with applicable ASTM standards for the applications indicated on the plans and specified here in.

## PART 3	EXECUTION

  - MACHINERY COVER AND BASE

The machinery cover and base shall be shop fabricated per the dimensions shown on the plans and details.  As much as practical, the machinery cover and base shall be shop assembled.  The contractor shall be responsible for making field measurements to ensure proper fit and anchorage of replacement machinery cover and base.  Any damage to the galvanized coating shall be repaired in accordance with Section 3.2.D. – 3.2.H. of this Specification division.

3.2 	HANDRAIL

- As much as practical, shop assemble all miscellaneous metal items.  Make field measurements prior to shop assembly to ensure proper fit of shop fabricated items.

- Install the handrail such that corners are square, vertical lines are plumb and handrail bases sit flush with the mounting surface.

- Protect the handrail against damage during shipment, storage and after installation while other work is being performed.

- All costs associated with repair of surfaces on which the zinc coating has been damaged in transporting, handling, or installing will be borne by the Contractor.

- Repair all areas where the underlying steel has been exposed or the coating thickness is less than 50 percent of the specified thickness or thickness equivalent.

- Provide a repair coating 1-1/2 times the thickness or thickness equivalent specified for galvanizing on the item but not less than 5 mils.  Thickness equivalent:  1 ounce of zinc per square of equals 1.7 mils.

- Use either zinc-based solder, zinc-rich paint, or sprayed zinc according to ASTM A780.

- Clean the metal and apply the coating according to ASTM A780 except as modified here.

  - If zinc-based solder is used for repair, use temperature sensitive crayons to verify the preheat temperatures of the metal before depositing the zinc alloy.

  - If zinc-rich paint is used for repair, clean the damaged surface to near-white metal before applying paint.  Apply the paint according to the manufacturer’s recommendations for temperature and dryness.

  - All holes made in the handrail in order to aid the hot-dipped galvanizing process shall be filled by welding additional material to the handrail, grinding the weld smooth and cold-galvanizing the weld area.

3.3	HOIST CHAINS

A.	All the tools, equipment and labor required to complete the work specified here shall be furnished by the Contractor.

B.	The existing hoist chains shall be replaced with the new chains only by removing the chain guard, which shall be painted on all surfaces as per the detailed specifications section 09900 “PAINTING”.

C.	Before starting any work on the chain replacement, the Contractor shall ask the Owner for the necessary power shut off and the gate shall be in the closed position.  Attention shall be paid such that no component shall be removed unless all mating connections, etc. are properly blocked, supported, fastened or arranged to allow no torque, bearing or stress on the part to be removed.  All the items to be removed and reassembled shall be carefully marked so that they can be reassembled in their proper and exact relationship.

D.	When installing the new chain, care shall be taken such that there are a minimum of two (2) holding turns on each drum with the gate in the closed position and there is no slack in the chain.  Also, there shall be no more than three (3) turns on the drum.  Also, the tension in both the chains of a gate shall be same so that the gate operates properly and smoothly.  Care shall be taken that when the gate is resting at the bottom concrete, the chain has no slackness.  The Contractor shall coat the chains and drum with grease prior to completion of this item of work with grease provided by the City.

E.	The Contractor shall request the Owner for calibration and testing the gate’s operation, only upon the completion of the installation of the new chains. Acceptance of chain replacement work for payment will not occur until the Owner’s successful completion of calibration and testing of the new chains.

3.4	FALL PROETECTION EQUIPMENT

A.	All the tools, equipment and labor required to complete the work specified here shall be furnished by the Contractor.

B.	The new fall protection equipment shall be installed per the manufacturer’s recommendations.

# END OF SECTION

Section 07920

NEOPRENE SEALS

PART 1	GENERAL

This specification covers the replacement of the side and bottom seals for the spillway gates.  Locations of seals are shown on the Detailed Drawing Sheets in Appendix A.   All the tools, equipment and labor for work shall be furnished by the Contractor.

PART 2	MATERIALS

The replacement seals shall be furnished by the City of Ann Arbor and provided to the Contractor.  The Contractor shall furnish and replace all fasteners in accordance with Detailed Specification Section 05500 “METAL FABRICATIONS”.

PART 3	EXECUTION

3.1	REPLACEMENT WORK

A.	The existing seals are to be replaced with the new seals only by removing the clamp angles and clamp bars, which are to be painted on all surfaces as per the Detailed Specifications Section 09900 “PAINTING”.  The surfaces on which the new seals are to be placed shall also be painted per Detailed Specifications Section 09900 “PAINTING”.  Prior to installation of new seals, the surface on which the new seals are to be placed shall be free from dust, rust, scale and all other foreign matter.  The Contractor shall submit product data for any product proposed to be used to clean the gate bottom or sides.  Each seal shall be furnished in a single piece. Pre-drill the holes in the new seals needed to attach the new seals to the gate.   The joints at the corners shall be cold cemented as per the manufacturer’s recommendations, and this joint shall be water tight.  The extra length, if any, shall be cut to the required length only after the seal has been clamped in position.

B.	During the replacement of the bottom seals, the Contractor shall clean the surface of contact of the seal and concrete so that this surface is free of all dirt, dust and any other foreign matter.  Any chemicals used to clean the gate surface shall not cause an adverse chemical reaction with the new seals.  The Contractor shall submit product data for any product proposed to be used to clean the gate bottom or sides.

3.2	ACCEPTANCE OF WORK

The seals replacement work shall be accepted for payment only if no visible leakage across the seals is observed when the level behind the closed gate is up to the top of the gate, below the level of wave deflector, if present.  The Contractor shall note that there is no allowable leakage across the seals.  Should leakage be observed after installation, the Contractor shall make repairs to the installed seals prior to acceptance and payment.  If repairs are not feasible, the Contractor shall remove and replace the seals at his/her expense with material purchased by the City.

END OF SECTION

# Section 09900

# PAINTING

## PART 1	GENERAL

1.1	REFERENCES

A.	ASTM D 16 - Terminology Relating to Paint, Varnish, Lacquer, and Related Products.

B.	ASTM D 4263 - Indicating Moisture in Concrete by the Plastic Sheet Method.

C.	ASTM F 1869 - Measuring Moisture Vapor Emission Rate of Concrete Subfloor Using Anhydrous Calcium Chloride.

D.	SSPC-SP 1 - Solvent Cleaning.

E.	SSPC-SP 2 - Hand Tool Cleaning.

F.	SSPC-SP 3 - Power Tool Cleaning.

G.	SSPC-SP 5/NACE 1 - White Metal Blast Cleaning.

H.	SSPC-SP 6/NACE 3 - Commercial Blast Cleaning.

- SSPC-SP 10/NACE 2 - Near-White Metal Blast Cleaning.

J.	SSPC-SP 13/NACE 6 - Surface Preparation of Concrete.

1.2	DEFINITIONS

A.	Definitions of Painting Terms:  ASTM D 16, unless otherwise specified.

B.	Dry Film Thickness (DFT):  Thickness of a coat of paint in fully cured state measured in mils (1/1000 inch).

1.3	SUBMITTALS

A.	Product Data:  Submit manufacturer's product data for each coating, including generic description, complete technical data, surface preparation, and application instructions.

B.	Color Samples:  Submit manufacturer’s color samples showing full range of standard colors.

C.	Manufacturer’s Quality Assurance:  Submit manufacturer’s certification that coatings comply with specified requirements and are suitable for intended application.

D.	Applicator’s Quality Assurance:  Submit list of a minimum of 3 completed projects of similar size and complexity to this Work completed within the last 5 years.  Projects shall demonstrate experience working on dams or other comparable structures (eg. – bridges, piers, locks, etc.) located on or over waterways.  Include for each project:

1.	Project name and location.

2.	Name of project owner, include a contact name and phone number.

3.	Name of general contractor if different than Contractor holding this contract.

4.	Name of engineer, include a contact name and phone number.

5.	Name of coating manufacturer.

6.	Approximate area of coatings applied.

7.	Date of completion.

1.4	QUALITY ASSURANCE

A.	Manufacturer’s Qualifications:

1.	Specialize in manufacture of coatings with a minimum of 10 years successful experience.

2.	Able to demonstrate successful performance on comparable projects.

3.	Single Source Responsibility:  Coatings shall be products of a single manufacturer.

B.	Applicator’s Qualifications:

1.	Experienced in application of specified coatings for a minimum of 5 years on projects of similar size and complexity to this Work.

- Applicator's Personnel:  Employ persons trained for application of specified coatings.

C.	Preapplication Meeting:  Convene a preapplication meeting before start of application of coating systems.  Require attendance of parties directly affecting work of this section, including Contractor, Owner, testing agency, applicator, and manufacturer’s representative.  Review the following:

1.	Environmental requirements.

2.	Protection of surfaces not scheduled to be coated.

3.	Surface preparation.

4.	Application.

5.	Repair.

6.	Field quality control.

7.	Cleaning.

8.	Protection of coating systems.

9.	One-year inspection.

10.	Coordination with other work.

1.5	DELIVERY, STORAGE, AND HANDLING

A. 	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying:

1.	Coating or material name.

2.	Manufacturer.

3.	Color name and number.

4.	Batch or lot number.

5.	Date of manufacture.

6.	Mixing and thinning instructions.

B.	Storage:

1.	Store materials in a clean dry area and within temperature range in accordance with manufacturer's instructions.

2.	Keep containers sealed until ready for use.

a.	Do not use materials beyond manufacturer’s shelf life limits.

C.	Handling:  Protect materials during handling and application to prevent damage or contamination.

1.6	ENVIRONMENTAL REQUIREMENTS

A.	Weather:

1.	Air and Surface Temperatures:  Prepare surfaces and apply and cure coatings within air and surface temperature range in accordance with manufacturer’s instructions.

2.	Surface Temperature:  Minimum of 5 degrees F (3 degrees C) above dew point.

3.	Relative Humidity:  Prepare surfaces and apply and cure coatings within relative humidity range in accordance with manufacturer’s instructions.

4.	Precipitation:  Do not prepare surfaces or apply coatings in rain, snow, fog, or mist.

5.	Wind:  Reinforce painting enclosure such that the enclosure will adequately protect the workers and the work in high winds.

B.	Ventilation:  Provide ventilation during coating evaporation stage in confined or enclosed areas in accordance with AWWA D 102.

C.	Dust and Contaminants:

1.	Schedule coating work to avoid excessive dust and airborne contaminants.

2.	Protect work areas from excessive dust and airborne contaminants during coating application and curing.

3.	Protect surface water from inclusion of dust from paint removal operations and paint from application operations.  Absolutely no paint, dust, sandblasting materials or other debris shall be allowed to enter the water of the Huron River.

4.	Should any contamination of the river occur, the Contractor shall immediately stop work and remove the contaminants from the river.  The Contractor shall also contact MDEQ Land and Water Division to notify this division that contamination has occurred.  The Contractor may be subject to fines and/or criminal penalties should the MDEQ determine that contamination occurred due to negligence on the part of the Contractor.

##### PART 2	PRODUCTS

2.1	MANUFACTURER

- Tnemec Company Incorporated, 121 S. Barnard Street, Suite 8, Howell, MI 48843 Phone: 517-540-0038 Fax: 517-540-0041.Web Site www.tnemec.com.

  - NON-IMMERSION SYSTEM FOR STEEL

Sluice Gate Chain Hoist Cowls, Walkway Structural Steel and Machinery Cover and Base (carbon steel replacement alternate ONLY)

1.	Surface Preparation:  SSPC-SP10 Near White Blast Cleaning

2.	Primer: Series 91K-97 Tneme-Zinc.  DFT 2.5 to 3.5 mils.

3.	Intermediate Coat: Series 69 Hi-Build Epoxoline II.  DFT 3.0 to 4.0 mils.

4.	Finish Coat:  Series 1075 Endura-Shield II. DFT 2.0 to 3.0 mils.

5.	Total DFT:  7.5 to 10.5 mils.

6.	Finish Color: As selected by Owner from manufacturer’s standard colors.

  - IMMERSION SYSTEM FOR STEEL

All Gate Components.

1.          System Type: Zinc/Epoxy/Epoxy

2.          Surface Preparation:  SSPC-SP10 Near White Blast Cleaning

3.          Primer: Series 91K-97 Tneme-Zinc. DFT 2.5 to 3.5 mils

4.          Intermediate Coat : Series 69 High-Build Epoxoline II. DFT 3.0 to 4.0 mils

5.          Finish Coat: Series 69 High-Build Epoxoline II. DFT 3.0 to 4.0 mils

6.          Total DFT: 8.5 to 11.5 mils.

7.           Finish color: As selected by Owner from manufacturer’s standard colors.

2.4	ACCESSORIES

A.	Coating Application Accessories:

1.	Accessories required for application of specified coatings in accordance with manufacturer’s instructions, including thinners.

  - Products of coating manufacturer, or compatible with coatings.

## PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas and conditions under which coating systems are to be applied.  Notify Owner of areas or conditions not acceptable.  Do not begin surface preparation or application until unacceptable areas or conditions have been corrected.

B.	The gate may be set in a partially open position to assist the Contractor throughout the blasting and painting operations.  The Contractor shall coordinate the desired gate position with the Owner.

  - PREPARATION

- Noise Control: The Contractor shall be guided by the City’s noise control ordinance.  A copy of the ordinance can be obtained from the City Clerk’s office or on the City’s web site:  www.a2gov.org.

- Dust and Sand Control:  The Contractor shall provide, operate and maintain an adequate means of dust control, by providing a barrier to control the spreading of sand, dust, and paint to the surrounding area so as not to disturb the people living in the area around the work site, or to contaminate the surface waters of the Huron River.  The Contractor shall submit a dust and sand control plan, to be approved by the Owner, prior to the start of work.

- Disposal of Sand Blasted Materials:  The sand blasted material is to be disposed of at an approved landfill.  It is the Contractor’s responsibility to determine if any hazardous waste is included in the materials to be disposed.

- Access to Dam Walkway Structural Steel:  The dam walkway is comprised of a pressure treated lumber deck supported by structural steel members.  The walkway deck must be removed to provide access to the entirety of the structural members.  The Contractor shall be responsible for the removal, storage and replacement of the dam walkway decking.  Removing, storing and replacing the walkway deck shall be the Contractor’s responsibility and is incidental to the Contract.

3.2	PROTECTION OF SURFACES NOT SCHEDULED TO BE COATED

A.	The Contractor shall take precautions to protect the sluice gate side seal heating system and oil wells.  The Owner will assist the Contractor in identifying this equipment in the field.

B.	Protect surrounding areas and surfaces not scheduled to be coated from damage during surface preparation and application of coatings.

C.	Immediately remove coatings that fall on surrounding areas and surfaces not scheduled to be coated.

3.3	SURFACE PREPARATION OF STEEL

A.	Prepare steel surfaces in accordance with coating system manufacturer’s instructions, and to preparation standard indicated for the system being applied.

B.	Fabrication Defects:

1.	Correct steel and fabrication defects revealed by surface preparation.

2.	Remove weld spatter and slag.

3.	Round sharp edges and corners of welds to a smooth contour.

4.	Smooth weld undercuts and recesses.

5.	Grind down porous welds to pinhole-free metal.

6.	Remove weld flux from surface.

- Ensure surfaces are dry.

- Exterior Exposed or Interior Exposed Surfaces:  Remove visible oil, grease, dirt, dust, mill scale, rust, paint, oxides, corrosion products, and other foreign matter in accordance with SSPC-SP 6/NACE 3.

- Abrasive Blast-Cleaned Surfaces:  Coat abrasive blast-cleaned surfaces with primer before visible rust forms on surface.  Do not leave blast-cleaned surfaces uncoated for more than 8 hours

  - SURFACE PREPARATION OF GALVANIZED STEEL  AND NONFERROUS METAL

A.	Prepare galvanized steel and nonferrous metal surfaces in accordance with coating system manufacturer’s instructions.

B.	Surface preparation recommendations will vary depending on substrate and exposure conditions.

C.	Ensure surfaces are dry.

D.	Remove Rust From Galvanized Steel:

1.	Remove white rust from galvanized steel by hand or power brushing.

2.	Remove rust from old galvanized steel in accordance with SSPC-SP 2 or SP 3.

3.	Do not damage or remove galvanizing.

F.	Increase mechanical adhesion under moderate to severe conditions, such as exterior exposure or chemical environments, by abrasive blast and/or chemical cleaning.

3.5	SURFACE PREPARATION OF DUCTILE OR CAST IRON

A.	Prepare ductile or cast iron surfaces in accordance with coating system manufacturer’s instructions.

B.	Ensure surfaces are clean, dry, and free of oil, grease, dirt, dust, and other contaminants.

3.6	APPLICATION

A.	Apply coatings in accordance with manufacturer's instructions.  Spray application of paint shall not be allowed under this contract.

B.	Mix and thin coatings, including multi-component materials, in accordance with manufacturer’s instructions.

C.	Keep containers closed when not in use to avoid contamination.

- Do not use mixed coatings beyond pot life limits.

- Use application equipment, tools, pressure settings, and techniques in accordance with manufacturer’s instructions.

- All coatings shall be applied only during good painting weather.  Surface temperature and ambient humidity shall be within limits prescribed by the manufacturer for the coating applied. No paint shall be applied when it is expected that the relative humidity will exceed 85% or that the air temperature will drop below 40° F within 18 hours after the application of the paint.  No painting shall be done when the ambient temperature is below 40° F.

G.	Uniformly apply coatings at spreading rate required to achieve specified DFT.

H.	Apply coatings to be free of film characteristics or defects that would adversely affect performance or appearance of coating systems.

I.	Stripe paint with brush critical locations on steel such as welds, corners, and edges using specified primer.

3.7	REPAIR

A.	Materials and Surfaces Not Scheduled To Be Coated:  Repair or replace damaged materials and surfaces not scheduled to be coated, which were damaged during and by painting and preparation operations.

B.	Damaged Coatings:  Touch-up or repair damaged coatings.  Touch-up of minor damage shall be acceptable where result is not visibly different from adjacent surfaces.  DFT minimum requirements must be met upon completion of touch-up to damaged areas. Recoat entire surface where touch-up result is visibly different, either in sheen, texture, or color.

C.	Coating Defects:  Repair in accordance with manufacturer’s instructions coatings that exhibit film characteristics or defects that would adversely affect performance or appearance of coating systems.

3.8	FIELD QUALITY CONTROL

A.	Inspector’s Services:  The Contractor shall hire Dixon Engineering or NTH (third party satisfactory to the Owner), at no additional expense to the Owner, to perform field inspections of items 1-4 below and prepare the field inspection reports described in item 5 below :

1.	Verify coatings and other materials are as specified.

2.	Verify surface preparation and application are as specified.

3.	Verify DFT of each coat and total DFT of each coating system are as specified using wet film and dry film gauges.

4.	Coating Defects:  Check coatings for film characteristics or defects that would adversely affect performance or appearance of coating systems.  Check for holidays on steel surfaces coated with immersion paint system using holiday detector.

5.	Report:

a.	Submit written reports describing inspections made and actions taken to correct nonconforming work.

b.	Report nonconforming work not corrected.

c.	         Submit copies of report to Owner and Contractor.

B. 	Determination of Film Thickness:  Randomly selected areas, each of at least 107.5 contiguous square feet, totaling at least 5% of the entire control area shall be tested.  Within this area, at least 5 squares, each of 7.75 square inches, shall be randomly selected.  Three readings shall be taken in each square, from which the mean film thickness shall be calculated.  No more than 20 percent of the mean film thickness measurements shall be below the specified thickness.  No single measurement shall be below 80 percent of the specified film thickness.  Total dry film thickness greater than twice the specified film thickness shall not be acceptable.  Areas where the measured dry film thickness exceeds twice that specified shall be completely recoated unless otherwise approved by the Owner. When measured dry film thickness is less than that specified additional coats shall be applied as required.

C. 	Holiday testing procedure and requirements:  Holiday test painted ferrous metal surfaces which will be submerged in water or other liquids, or surfaces which are enclosed in a vapor space in such structures. Mark areas which contain holidays.  Repair or repaint in accordance with paint manufacturer's printed instructions and retest.

1.	Dry Film Thickness of 20 Mils or Less:  For surfaces having a total dry film thickness of 20 mils or less:  Tinker & Rasor Model M1 non-destructive type holiday detector, K-D Bird Dog, shall be used.  The unit shall operate at less than 75-volts.  For thicknesses between 10 and 20 mils, a non-sudsing type wetting agent, such as Kodak Photo-Flow, shall be added to the water prior to wetting the detector sponge.

3.9      CLEANING

- Remove temporary coverings and protection of surrounding areas and surfaces.  The Contractor shall remove all dust, sand and debris from work space enclosure prior to removal.  The Contractor shall use extreme caution while removing protection equipment and work space enclosure as to not allow any sand, dust, debris and/or paint collected on equipment from entering the surface waters of the Huron River.  The sand blasting media shall not be allowed to be spilled upon the ground and shall be properly disposed of in accordance with Detailed Specification Section 01000 “GENERAL REQUIREMENTS”.

3.10	ACCEPTANCE OF WORK

The painting work will be accepted for payment upon successful removal of work space enclosure without contamination of the Huron River, the dam walkway decking has been replaced in a condition that is equal to or better than the existing condition, and the painted surfaces have been successfully tested for correct DFT and holidays.

# END OF SECTION

# SPECIAL PROVISIONS

1.0	TRANSPORTING AND POSITIONING OF STOP-LOGS

A.	GENERAL

1.	This Special Provision covers the transportation of the stop-logs from Barton Pump Station, 1010 West Huron River Drive, Ann Arbor, Michigan 48103, to Superior Dam, 6000 First Street, Ypsilanti, Michigan 48198 and positioning of the stop-logs at Superior Dam.

2.	All of the tools, equipment and labor required for the work specified in this Special Provision shall be furnished by the Contractor.

B.	MATERIALS

The stop-logs are the property of the City of Ann Arbor and will be furnished to the Contractor for the duration of this project.  Should the Contractor find that the existing gaskets on the stop-logs inadequate to provide for a water-tight fit along the river channel bottom, the Contractor may replace such gaskets at his/her expense.

C.	EXECUTION

1.	Refer to sheet 9 of 9 for stop-log placement.  Each stop-log is a set of three identical sections, except for sluice gates, which is a set of two identical sections.  The set for Geddes Dam North Spillway shall be used for the Superior Dam Spillway, by making a slight modification to the stop-log (the modification shall be done by the Contractor, refer to details for stop logs).  Each section of the stop-log weighs approximately 4,000 lbs.  The Owner will assist the Contractor in identifying the correct set of stop-logs.

2.	Before placing stop-logs into position, the Contractor shall inspect the existing gaskets on the stop-logs for defects that may prevent a water-tight seal along the edge and bottom of the stop-log channel.  The Contractor may replace the existing neoprene seals with the new ones, only along the sides and bottom of the stop-log at his/her expense.  The surface on which the neoprene is to be replaced shall be free of rust, scales and all other foreign matter to insure the proper bonding of the neoprene with the stop-log.  The neoprene shall be glued to the stop-log per the manufacturer’s recommendations.  Each seal shall be fixed in such a manner that it provides a watertight joint.

3.	The Contractor shall be responsible for any dewatering of the work area that the Contractor deems necessary in order to conduct the work included with this Contract.  This work may include, but may not be limited to pumping of water from between the stop logs and sluice gate, removal of debris from bottom of stop log channel prior to placement (this work has been performed by professional divers on past projects), and/or cleaning of the stop-log channels.

END OF SECTION

APPENDIX A

DETAILED DRAWINGS

APPENDIX B

PRODUCT DATA